Last data updates: 15 January 2015

Ho, Y.S. and Ofomaja, A.E. (2006), Biosorption thermodynamics of cadmium on coconut copra meal as biosorbent. Biochemical Engineering Journal, 30 (2), 117-123.

| Document type: Article | Language: English | Cited references: 28 | Times cited: 107 | Times self cited: 10 |
| --- | --- | --- | --- | --- |

Abstract: Coconut copra meal, a waste product of coconut oil production was investigated for its potential use as a biosorbent for cadmium ions from an aqueous solution. A comparison of linear least-squares method and a trial and error non-linear method of three widely used isotherms, Langmuir, Freundlich, and Redlich-Peterson, were examined. Langmuir isotherm parameters obtained from the four Langmuir linear equations by using linear method were not similar, but were the same when non-linear method was used. The best-fitting isotherms were Langmuir and Redlich-Peterson isotherms. Langmuir isotherm is a special case of Redlich-Peterson isotherm when constant g is unity. In addition, various thermodynamic parameters, such as Delta G degrees, Delta H degrees, and Delta S degrees, were calculated. The biosorption process is a spontaneous and exothermic process. (c) 2006 Elsevier B.V. All rights reserved.

Author Keywords: copra meal; cadmium ions; langmuir isotherm; temperature; adsorption

KeyWords Plus: Low-Cost Adsorbent; Aqueous-Solution; Tree Fern; Waste-Water; Sorption Isotherm; Adsorption; Removal; Equilibrium; Cd(II); Copper

Addresses: Ho YS (reprint author), Peking Univ, Coll Environm Sci, Dept Environm Sci, Beijing, 100871 Peoples R China

Peking Univ, Coll Environm Sci, Dept Environm Sci, Beijing, 100871 Peoples R China

Univ Benin, Fac Sci, Dept Chem, Benin, Nigeria

E-mail Addresses: dr_ysho@hotmail.com

- Gupta, V.K., Nayak, A., Bhushan, B. and Agarwal, S. (2015), A Critical Analysis on the Efficiency of Activated Carbons from Low-Cost Precursors for Heavy Metals Remediation. Critical Reviews in Environmental Science and Technology, 45 (6), 613-668.

- Das, D., Varshini, C.J.S. and Das, N. (2014), Recovery of lanthanum(III) from aqueous solution using biosorbents of plant and animal origin: Batch and column studies. Minerals Engineering, 69), 40-56.

- Barot, N.S., Khilnani, R.P. and Bagla, H.K. (2014), Biosorptive profile of synthetic and natural humiresin for the remediation of metallic water pollutants. Journal of Radioanalytical and Nuclear Chemistry, 302 (2), 951-959.

- Kir, E., Celik, M., Sevinc, G., Karipcin, F. and Dede, B. (2014), Synthesis, characterization, and sorption properties of silica gel-immobilized Schiff base derivatives. Desalination and Water Treatment, 52 (34-36), 6530-6541.

- Ghasemi, M., Ghasemi, N., Zahedi, G., Alwi, S.R.W., Goodarzi, M. and Javadian, H. (2014), Kinetic and equilibrium study of Ni(II) sorption from aqueous solutions onto Peganum harmala-L. International Journal of Environmental Science and Technology, 11 (7), 1835-1844.

- Wu, F.C., Wu, P.H., Tseng, R.L. and Juang, R.S. (2014), Use of refuse-derived fuel waste for the adsorption of 4-chlorophenol and dyes from aqueous solution: Equilibrium and kinetics. Journal of the Taiwan Institute of Chemical Engineers, 45 (5), 2628-2639.

- Ozdemir, U., Ozbay, B., Ozbay, I. and Veli, S. (2014), Application of Taguchi L-32 orthogonal array design to optimize copper biosorption by using Spaghnum moss. Ecotoxicology and Environmental Safety, 107), 229-235.

- Varsihini, C.J.S., Das, D. and Das, N. (2014), Optimization of parameters for cerium(III) biosorption onto biowaste materials of animal and plant origin using 5-level Box-Behnken design: Equilibrium, kinetic, thermodynamic and regeneration studies. Journal of Rare Earths, 32 (8), 745-758.

- Basak, G., Das, D. and Das, N. (2014), Enhanced Zn(II) uptake using zinc imprinted form of novel nanobiosorbent and its application as an antimicrobial agent. Korean Journal of Chemical Engineering, 31 (5), 812-820.

- Jaafarzadeh, N., Teymouri, P., Babaei, A.A., Alavi, N. and Ahmadi, M. (2014), Biosorption of Cadmium (Ii) from Aqueous Solution by Nacl-Treated Ceratophyllum Demersum. Environmental Engineering and Management Journal, 13 (4), 763-773.

- Omorogie, M.O., Babalola, J.O., Unuabonah, E.I. and Gong, J.R. (2014), Hybrid materials from agro-waste and nanoparticles: implications on the kinetics of the adsorption of inorganic pollutants. Environmental Technology, 35 (5), 611-619.

- Zhang, Z.Q. and Zhang, J. (2014), Characteristics of Cadmium(II) Adsorbed by the Extracellular Polymeric Substance Extracted from Waste-Activated Sludge After Short-Time Aerobic Digestion. Water Air and Soil Pollution, 225 (2.

- Dhir, B. (2014), Potential of biological materials for removing heavy metals from wastewater. Environmental Science and Pollution Research, 21 (3), 1614-1627.

- Nosal-Wiercinska, A. (2014), Influence of temperature on the reduction kinetics of Bi(III) ion in the presence of cystine in chlorate (VII) solutions of decreased water activity. Central European Journal of Chemistry, 12 (2), 213-219.

- Faghihian, H., Nasrabadi, S.N. and Khonsari, S. (2014), Removal of Sr(II) from Aqueous Solutions by Aminosilane Functionalized MCM-48. Separation Science and Technology, 49  (13), 2031-2038.

- Suresh, C., Reddy, D.H.K., Harinath, Y., Naik, B.R., Seshaiah, K. and Reddy, A.V.R. (2014), Development of Wood Apple Shell (Feronia acidissima) Powder Biosorbent and Its Application for the Removal of Cd(II) from Aqueous Solution. Scientific World Journal, .

- Sim, S.F., Lee, T.Z.E., Lu, N.A.L.M. and Murtedza, M. (2014), Modified Coconut Copra Residues as a Low Cost Biosorbent for Adsorption of Humic Substances from Peat Swamp Runoff. Bioresources, 9 (1), 952-968.

- Johari, K., Sarnan, N., Song, S.T., Mat, H. and Stuckey, D.C. (2013), Utilization of Coconut Milk Processing Waste as a Low-Cost Mercury Sorbent. Industrial & Engineering Chemistry Research, 52 (44), 15648-15657.

- Zolgharnein, J., Asanjarani, N. and Shariatmanesh, T. (2013), Taguchi L-16 orthogonal array optimization for Cd (II) removal using Carpinus betulus tree leaves: Adsorption characterization. International Biodeterioration & Biodegradation, 85), 66-77.

- Khan, S.B., Rahman, M.M., Marwani, H.M., Asiri, A.M. and Alamry, K.A. (2013), An assessment of zinc oxide nanosheets as a selective adsorbent for cadmium. Nanoscale Research Letters, 8.

- Panahi, H.A., Feizbakhsh, A., Fard, R.A. and Moniri, E. (2013), Quantitative analysis and sorption of cadmium in environmental samples with a functionalized synthetic polymer. Toxicological and Environmental Chemistry, 95 (8), 1279-1289.

- Shakerin, N., Zolriasatain, F., Panahi, H.A. and Moniri, E. (2013), Preconcentration of samarium with modified yeast cells for its determination by atomic emission spectroscopy. Toxicological and Environmental Chemistry, 95 (8), 1290-1298.

- Panahi, H.A., Nezhati, M.N., Kashkoieh, R.A., Moniri, E. and Galaev, I.Y. (2013), Poly[1-(N,N-bis-carboxymethyl)amino-3-allylglycerol-co-dimethylacrylamid e] brushes grafted onto siliceous support for preconcentration and determination of cobalt (II) in human plasma and environmental samples.  Korean Journal of Chemical Engineering, 30 (9), 1722-1728.

- Zhao, X., Zhao, Q.L., Meng, Q.Q., Xia, W. and Ye, Z.F. (2013), Reductions in cod and acute toxicity of wastewater generated from refined cotton production using activated carbon fibre (ACF). Canadian Journal of Chemical Engineering, 91 (6), 1069-1076.

- Panahi, H.A., Karimi, M., Adinehlo, H., Nezhati, M.N., Moniri, E., Kelahrodi, S.R., Manoochehri, M., Azizi, Z. and Feizbakhsh, A. (2013), Uptake of lead(II) from water sample by 2-allyl-phenol-functionalized amberlite XAD-4: isotherm and thermodynamic study. Desalination and Water Treatment, 51 (16-18), 3114-3124.

- Moniri, E., Panahi, H.A., Karimi, M., Rajabi, N.A. and Faridi, M. (2013), Chemical Modification of Amberlite XAD-2 by Immobilization of Calcein Blue for Extractive Concentration of Lead(II) Ion in Environmental Samples. Advances in Polymer Technology, 32), E462-E473.

- Al-Ghamdi, A., Altaher, H. and Omar, W. (2013), Application of date palm trunk fibers as adsorbents for removal of Cd+2 ions from aqueous solutions. Journal of Water Reuse and Desalination, 3 (1), 47-54.

- Li, C.H. and Xu, W. (2013), Adsorption and removal of As (V) from drinking water using D301-Fe. Energy Engineering and Environmental Engineering, Pts 1and 2, 316-317), 754-757.

- Gochev, V., Velkova, Z., Stoytcheva, M., Yemendzhiev, H., Aleksieva, Z. and Krastanov, A. (2012), Biosorption of Cu(Ii) from Aqueous Solutions by Immobilized Mycelium of Trametes Versicolor. Biotechnology & Biotechnological Equipment, 26 (6), 3365-3370.

- Sadeghi, H.B., Panahi, H.A., Ghasemi, M., Moniri, E. and Galaev, I.Y. (2012), Determination of neodymium (III) in human plasma and environmental samples with poly(allyl glycidyl ether/iminodiacetic acid- co-dimethylacrylamide) brushes grafted onto siliceous support. Advances in Polymer Technology, 31 (4), 257-270.

- Panahi, H.A., Mehmandost, N., Moniri, E. and Galaev, I.Y. (2012), Iminodiacetic acid-containing polymer brushes grafted onto silica gel for preconcentration and determination of copper(II) in environmental samples. Journal of Applied Polymer Science, 126 (2), 480-489.

- Qayoom, A. and Kazmi, S.A. (2012), Effect of Temperature on Equilibrium and Thermodynamic Parameters of Cd (II) Adsorption onto Turmeric Powder. Journal of the Chemical Society of Pakistan, 34 (5), 1084-1090.

- Moniri, E., Panahi, H.A., Jalal, M.M. and Gaforiyan, H. (2012), Isotherm Study and Interaction Consideration of Samarium(III) with New Modified Siliceous Support. Asian Journal of Chemistry, 24 (10), 4253-4256.

- Zheng, L.C., Zhu, C.F., Dang, Z., Zhang, H., Yi, X.Y. and Liu, C.Q. (2012), Preparation of cellulose derived from corn stalk and its application for cadmium ion adsorption from aqueous solution. Carbohydrate Polymers, 90 (2), 1008-1015.

- Kalal, H.S., Panahi, H.A., Hoveidi, H., Taghiof, M. and Menderjani, M.T. (2012), Synthesis and application of Amberlite xad-4 functionalized with alizarin red-s for preconcentration and adsorption of rhodium (III). Iranian Journal of Environmental Health Science & Engineering, 9.

- Nosal-Wiercinska, A. (2012), Electrochemical and thermodynamic study of the electroreduction of Bi(III) ions in the presence of cysteine in solutions of different water activity. Journal of Electroanalytical Chemistry, 681), 103-108.

- Panahi, H.A., Sadeghi, H.B., Farahmandnejad, N., Badr, A.R. and Moniri, E. (2012), Removal of cobalt from human serum and environmental samples by adsorption using Amberlite XAD-2-salicylic acid-iminodiacetic acid. Desalination and Water Treatment, 46 (1-3), 244-255.

- Panahi, H.A., Abdouss, M., Ghiabi, F., Moniri, E. and Shoushtari, A.M. (2012), Modification and characterization of poly (ethylene terephthalate)-grafted-acrylic acid/acryl amide fiber for removal of lead from human plasma and environmental samples. Journal of Applied Polymer Science, 124 (6), 5236-5246.

- Kalal, H.S., Hoveidi, H., Thagiof, M., Pakizevand, N., Almasian, M.R. and Firoozzare, M.A. (2012), Pre-concentration and Determination of Platinum (IV) in Water Samples Using Chelating Resin by Inductively Coupled Plasma Atomic Emission Spectroscopy (ICP-AES). International Journal of Environmental Research, 6 (3), 739-750.

- Qu, J., Luo, C.Q., Cong, Q. and Yuan, X. (2012), Carbon nanotubes and Cu-Zn nanoparticles synthesis using hyperaccumulator plants. Environmental Chemistry Letters, 10 (2), 153-158.

- Saif, M.M.S., Kumar, N.S. and Prasad, M.N.V. (2012), Binding of cadmium to Strychnos potatorum seed proteins in aqueous solution: Adsorption kinetics and relevance to water purification. Colloids and Surfaces B-Biointerfaces, 94), 73-79.

- Reddy, D.H.K., Seshaiah, K., Reddy, A.V.R. and Lee, S.M. (2012), Optimization of Cd(II), Cu(II) and Ni(II) biosorption by chemically modified Moringa oleifera leaves powder. Carbohydrate Polymers, 88 (3), 1077-1086.

- Monteiro, C.M., Castro, P.M.L. and Malcata, F.X. (2012), Metal uptake by microalgae: Underlying mechanisms and practical applications. Biotechnology Progress, 28 (2), 299-311.

- Veneu, D.M., Pino, G.A.H., Torem, M.L. and Saint'Pierre, T.D. (2012), Biosorptive removal of cadmium from aqueous solutions using a Streptomyces lunalinharesii strain. Minerals Engineering, 29), 112-120.

- Kocyigit, O., Erdemir, S. and Yilmaz, M. (2012), Sorption of Cu(II) onto silica gel immobilized calix[4]arene derivative with tripodal structure. Journal of Inclusion Phenomena and Macrocyclic Chemistry, 72 (1-2), 137-147.

- Oladoja, N.A., Ololade, I.A., Olaseni, S.E., Olatujoye, V.O., Jegede, O.S. and Agunloye, A.O. (2012), Synthesis of Nano Calcium Oxide from a Gastropod Shell and the Performance Evaluation for Cr (VI) Removal from Aqua System. Industrial & Engineering Chemistry Research, 51 (2), 639-648.

- Barot, N.S. and Bagla, H.K. (2012), Studies on biosorption of Cr(VI) on a green resin: dry cow dung powder and tracer technique. Radiochimica Acta, 100 (11), 833-842.

- Ozel, H.U. (2012), Biosorption of Cd(Ii) Ions by Nordmann Fir Cones. Fresenius Environmental Bulletin, 21 (9), 2527-2535.

- Neto, V.D.S., Carvalho, T.V., Honorato, S.B., Gomes, C.L., Barros, F.C.F., raujo-Silva, M.A., Freire, P.T.C. and Nascimento, R.F. (2012), Coconut Bagasse Treated by Thiourea/Ammonia Solution for Cadmium Removal: Kinetics and Adsorption Equilibrium. Bioresources, 7 (2), 1504-1524.

- Panahi, H.A., Nezhati, M.N., Kashkoieh, R.A., Moniri, E. and Galaev, I.Y. (2012), A siliceous support grafted with poly[1-(N,N-bis-carboxymethyl)amino-3-allylglycerol-co-dimethylacrylamid e] brushes for removal of nickel from environmental samples. Toxicological and Environmental Chemistry, 94 (5), 860-872.

- Gangupomu, R.H., Kositkanawuth, K., Sattler, M.L., Ramirez, D., Dennis, B.H., MacDonnell, F.M., Billo, R. and Priest, J.W. (2012), Analysis and comparison of inertinite-derived adsorbent with conventional adsorbents. Journal of the Air & Waste Management Association, 62 (5), 489-499.

- Khani, M.H. (2011), Uranium biosorption by Padina sp algae biomass: kinetics and thermodynamics. Environmental Science and Pollution Research, 18 (9), 1593-1605.

- Panahi, H.A., Mottaghinejad, E., Badr, A.R. and Moniri, E. (2011), Synthesis, Characterization, and Application of Amberlite XAD-2-Salicylic Acid- Iminodiacetic Acid for Lead Removal from Human Plasma and Environmental Samples. Journal of Applied Polymer Science, 121 (2), 1127-1136.

- Moniri, E., Panahi, H.A., Karimi, M., Rajabi, N.A., Faridi, M. and Manoochehri, M. (2011), Modification and characterization of amberlite XAD-2 with calcein blue for preconcentration and determination of copper(II) from environmental samples by atomic absorption spectroscopy. Korean Journal of Chemical Engineering, 28 (7), 1523-1531.

- Kurniawan, A., Sisnandy, V.O.A., Trilestari, K., Sunarso, J., Indraswati, N. and Ismadji, S. (2011), Performance of durian shell waste as high capacity biosorbent for Cr(VI) removal from synthetic wastewater. Ecological Engineering, 37 (6), 940-947.

- Ofomaja, A.E. and Naidoo, E.B. (2011), Kinetic modeling of the interaction between copper(II) and calcium hydroxide treated pine cone powder. Journal of the Taiwan Institute of Chemical Engineers, 42 (3), 480-485.

- Chowdhury, S. and Saha, P. (2011), Adsorption Kinetic Modeling of Safranin onto Rice Husk Biomatrix Using Pseudo-first- and Pseudo-second-order Kinetic Models: Comparison of Linear and Non-linear Methods. Clean-Soil Air Water, 39 (3), 274-282.

- Ofomaja, A.E. (2011), Kinetics and pseudo-isotherm studies of 4-nitrophenol adsorption onto mansonia wood sawdust. Industrial Crops and Products, 33 (2), 418-428.

- Hubbe, M.A., Hasan, S.H. and Ducoste, J.J. (2011), Cellulosic Substrates for Removal of Pollutants from Aqueous Systems: A Review. 1. Metals. Bioresources, 6 (2), 2161-U2914.

- Basha, S., Murthy, Z.V.P. and Jha, B. (2011), Kinetics, Isotherms, and Thermodynamics of Hg(II) Biosorption onto Carica papaya. Bioremediation Journal, 15 (1), 26-34.

- Srivastava, P. and Hasan, S.H. (2011), Biomass of Mucor Heimalis for the Biosorption of Cadmium from Aqueous Solutions: Equilibrium and Kinetic Studies. Bioresources, 6 (4), 3656-3675.

- Zhang, M.H., Zhao, Q.L. and Ye, Z.F. (2011), Organic pollutants removal from 2,4,6-trinitrotoluene (TNT) red water using low cost activated coke. Journal of Environmental Sciences-China, 23 (12), 1962-1969.

- Pratibha, R., Malar, P., Rajapriya, T., Balapoornima, S. and Ponnusami, V. (2010), Statistical and equilibrium studies on enhancing biosorption capacity of Saccharomyces cerevisiae through acid treatment. Desalination, 264 (1-2), 102-107.

- Das, D., Das, N. and Mathew, L. (2010), Kinetics, equilibrium and thermodynamic studies on biosorption of Ag(I) from aqueous solution by macrofungus Pleurotus platypus. Journal of Hazardous Materials, 184 (1-3), 765-774.

- Bhatnagar, A., Vilar, V.J.P., Botelho, C.M.S. and Boaventura, R.A.R. (2010), Coconut-based biosorbents for water treatment - A review of the recent literature. Advances in Colloid and Interface Science , 160 (1-2), 1-15.

- Chakravarty, P., Sen Sarma, N. and Sarma, H.P. (2010), Biosorption of cadmium(II) from aqueous solution using heartwood powder of Areca catechu. Chemical Engineering Journal, 162 (3), 949-955.

- Yazdankhah, A., Moradi, S.E., Amirmahmoodi, S., Abbasian, M. and Shoja, S.E. (2010), Enhanced sorption of cadmium ion on highly ordered nanoporous carbon by using different surfactant modification. Microporous and Mesoporous Materials, 133 (1-3), 45-53.

- Panahi, H.A., Morshedian, J., Mehmandost, N., Moniri, E. and Galaev, I.Y. (2010), Grafting of polyp[1-(N,N-bis-carboxymethyl)amino-3-allylglycerol-co-dimethylacrylami de] copolymer onto siliceous support for preconcentration and determination of lead (II) in human plasma and environmental samples. Journal of Chromatography A, 1217 (32), 5165-5172.

- Zheng, L.C., Dang, Z., Zhu, C.F., Yi, X.Y., Zhang, H. and Liu, C.Q. (2010), Removal of cadmium(II) from aqueous solution by corn stalk graft copolymers. Bioresource Technology, 101 (15), 5820-5826.

- Wu, F.C., Liu, B.L., Wu, K.T. and Tseng, R.L. (2010), A new linear form analysis of Redlich-Peterson isotherm equation for the adsorptions of dyes. Chemical Engineering Journal, 162 (1), 21-27.

- Ofomaja, A.E., Naidoo, E.B. and Modise, S.J. (2010), Biosorption of copper(II) and lead(II) onto potassium hydroxide treated pine cone powder. Journal of Environmental Management, 91 (8), 1674-1685.

- Ofomaja, A.E., Naidoo, E.B. and Modise, S.J. (2010), Surface modification of pine cone powder and its application for removal of Cu(II) from wastewater. Desalination and Water Treatment, 19 (1-3), 275-285.

- Ofomaja, A.E. (2010), Equilibrium studies of copper ion adsorption onto palm kernel fibre. Journal of Environmental Management, 91 (7), 1491-1499.

- Zhang, M.H., Zhao, Q.L., Bai, X. and Ye, Z.F. (2010), Adsorption of organic pollutants from coking wastewater by activated coke. Colloids and Surfaces A-Physicochemical and Engineering Aspects, 362 (1-3), 140-146.

- Ofomaja, A.E., Unuabonah, E.I. and Oladoja, N.A. (2010), Competitive modeling for the biosorptive removal of copper and lead ions from aqueous solution by Mansonia wood sawdust. Bioresource Technology, 101 (11), 3844-3852.

- Ben Hamissa, A.M., Lodi, A., Seffen, M., Finocchio, E., Botter, R. and Converti, A. (2010), Sorption of Cd(II) and Pb(II) from aqueous solutions onto Agave americana fibers. Chemical Engineering Journal, 159 (1-3), 67-74.

- Liu, Q., Guo, H.M. and Shan, Y. (2010), Adsorption of fluoride on synthetic siderite from aqueous solution. Journal of Fluorine Chemistry, 131 (5), 635-641.

- Zheng, L.C., Dang, Z., Yi, X.Y. and Zhang, H. (2010), Equilibrium and kinetic studies of adsorption of Cd(II) from aqueous solution using modified corn stalk. Journal of Hazardous Materials, 176 (1-3), 650-656.

- Oladoja, N.A., Ofomaja, A.E., Idiaghe, J.A., Akinlabi, A.K. and Egbon, E.E. (2010), Sorption of Cu (II) ion from aqueous solution by scrap tyre. Desalination and Water Treatment, 16 (1-3), 83-94.

- Ofomaja, A.E., Naidoo, E.B. and Modise, S.J. (2010), Kinetic and Pseudo-Second-Order Modeling of Lead Biosorption onto Pine Cone Powder. Industrial & Engineering Chemistry Research,  49 (6), 2562-2572.

- Bhatnagar, A. and Sillanpaa, M. (2010), Utilization of agro-industrial and municipal waste materials as potential adsorbents for water treatment-A review. Chemical Engineering Journal, 157 (2-3), 277-296.

- Pandey, P.K., Sharma, S.K. and Sambi, S.S. (2010), Kinetics and equilibrium study of chromium adsorption on zeoliteNaX. International Journal of Environmental Science and Technology, 7 (2), 395-404.

- Rao, K.S., Anand, S. and Venkateswarlu, P. (2010), Psidium guvajava L Leaf Powder - A Potential Low-cost Biosorbent for the Removal of Cadmium(II) Ions from Wastewater. Adsorption Science & Technology, 28 (2), 163-178.

- Rao, K.S., Anand, S. and Venkateswarlu, P. (2010), Adsorption of Cadmium(Ii) Ions from Aqueous Solution by Tectona Grandis Lf (Teak Leaves Powder). Bioresources, 5 (1), 438-U26.

- Chen, C. and Wang, J.L. (2010), Removal of Heavy Metal Ions by Waste Biomass of Saccharomyces Cerevisiae. Journal of Environmental Engineering-Asce, 136 (1), 95-102.

- Febriana, N., Lesmana, S.O., Soetaredjo, F.E., Sunarso, J. and Ismadji, S. (2010), Neem leaf utilization for copper ions removal from aqueous solution. Journal of the Taiwan Institute of Chemical Engineers, 41 (1), 111-114.

- Wang, X.H. and Wang, A.Q. (2010), Adsorption Characteristics of Chitosan-g-Poly(acrylic acid)/Attapulgite Hydrogel Composite for Hg(II) Ions from Aqueous Solution. Separation Science and Technology, 45 (14), 2086-2094.

- Vazquez, G., Freire, M.D., Gonzalez-Alvarez, J. and Antorrena, G. (2009), Equilibrium and kinetic modelling of the adsorption of Cd2+ ions onto chestnut shell. Desalination, 249 (2), 855-860.

- Ofomaja, A.E., Naidoo, E.B. and Modise, S.J. (2009), Removal of copper(II) from aqueous solution by pine and base modified pine cone powder as biosorbent. Journal of Hazardous Materials, 168 (2-3), 909-917.

- Vazquez, G., Gonzalez-Alvarez, J., Freire, M.S., Calvo, M. and Antorrena, G. (2009), Determination of the Optimal Conditions for the Adsorption of Cadmium Ions and Phenol on Chestnut (Castanea Sativa) Shell. Global Nest Journal, 11 (2), 196-204.

- Liu, Y. (2009), Is the Free Energy Change of Adsorption Correctly Calculated? Journal of Chemical and Engineering Data, 54 (7), 1981-1985.

- Zhang, J., Xie, S.D. and Ho, Y.S. (2009), Removal of fluoride ions from aqueous solution using modified attapulgite as adsorbent. Journal of Hazardous Materials, 165 (1-3), 218-222.

- Lesmana, S.O., Febriana, N., Soetaredjo, F.E., Sunarso, J. and Ismadji, S. (2009), Studies on potential applications of biomass for the separation of heavy metals from water and wastewater. Biochemical Engineering Journal, 44 (1), 19-41.

- Febrianto, J., Kosasih, A.N., Sunarso, J., Ju, Y.H., Indraswati, N. and Ismadji, S. (2009), Equilibrium and kinetic studies in adsorption of heavy metals using biosorbent: A summary of recent studies. Journal of Hazardous Materials, 162 (2-3), 616-645.

- Khambhaty, Y., Mody, K., Basha, S. and Jha, B. (2009), Kinetics, equilibrium and thermodynamic studies on biosorption of hexavalent chromium by dead fungal biomass of marine Aspergillus niger. Chemical Engineering Journal, 145 (3), 489-495.

- Gupta, V.K., Carrott, P.J.M., Carrott, M.M.L.R. and Suhas. (2009), Low-Cost Adsorbents: Growing Approach to Wastewater Treatmenta Review. Critical Reviews in Environmental Science and Technology, 39 (10), 783-842.

- Arief, V.O., Trilestari, K., Sunarso, J., Indraswati, N. and Ismadji, S. (2008), Recent Progress on Biosorption of Heavy Metals from Liquids Using Low Cost Biosorbents: Characterization, Biosorption Parameters and Mechanism Studies. Clean-Soil Air Water, 36 (12), 937-962.

- Hameed, B.H., Mahmoud, D.K. and Ahmad, A.L. (2008), Sorption equilibrium and kinetics of basic dye from aqueous solution using banana stalk waste. Journal of Hazardous Materials, 158 (2-3), 499-506.

- Apiratikul, R. and Pavasant, P. (2008), Sorption of Cu(2+), Cd(2+), and Pb(2+) using modified zeolite from coal fly ash. Chemical Engineering Journal, 144 (2), 245-258.

- Zubieta, C.E., Messina, P.V., Luengo, C., Dennehy, M., Pieroni, O. and Schulz, P.C. (2008), Reactive dyes remotion by porous TiO2-chitosan materials. Journal of Hazardous Materials, 152 (2), 765-777.

- Hatay, I., Gup, R. and Ersoz, M. (2008), Silica gel functionalized with 4-phenylacetophynone 4-aminobenzoylhydrazone: Synthesis of a new chelating matrix and its application as metal ion collector. Journal of Hazardous Materials, 150 (3), 546-553.

- Balan, C., Biilba, D. and Macoveanu, M. (2008), Removal of cadmium (II) from aqueous solutions by sphagnum moss peat: Equilibrium study. Environmental Engineering and Management Journal, 7 (1), 17-23.

- Nouri, L., Ghodbane, I., Hamdaoui, O. and Chiha, M. (2007), Batch sorption dynamics and equilibrium for the removal of cadmium ions from aqueous phase using wheat bran. Journal of Hazardous Materials, 149 (1), 115-125.

- Sousa, F.W., Moreira, S.A., Oliveira, A.G., Cavalcante, R.M., Nascimento, R.F. and Rosa, M.F. (2007), The use of green coconut shells as adsorbents in the removal of toxic metals. Quimica Nova, 30 (5), 1153-1157.

- Mohan, D., Pittman, C.U., Bricka, M., Smith, F., Yancey, B., Mohammad, J., Steele, P.H., exandre-Franco, M.F., Gomez-Serrano, V. and Gong, H. (2007), Sorption of arsenic, cadmium, and lead by chars produced from fast pyrolysis of wood and bark during bio-oil production. Journal of Colloid and Interface Science, 310 (1), 57-73.

- Cestari, A.R., Vieira, E.F.S., Vieira, G.S. and Almeida, L.E. (2007), Aggregation and adsorption of reactive dyes in the presence of an anionic surfactant on mesoporous aminopropyl silica. Journal of Colloid and Interface Science, 309 (2), 402-411.

- Inbaraj, B.S. (2006), Comment on "adsorption of reactive dyes from a textile effluent using sawdust as the adsorbent". Industrial & Engineering Chemistry Research, 45 (21), 7362.