Last data updates: 23 April 2014

Zhang, L., Hong, S., He, J., Gan, F.X. and Ho, Y.S.* (2011), Adsorption characteristic studies of phosphorus onto laterite. Desalination and Water Treatment, 25 (1), 98-105.

| Document type: Article | Language: English | Cited references: 17 | Times cited: 6 | Times self cited: 0 |
| --- | --- | --- | --- | --- |

Abstract: Soil has been widely used in many wastewater treatment systems, and proved to be an effective substrate for phosphorus removal and retention. It is significant to study its adsorption characteristics by using appropriate theoretical models. In this study, laterite (or red soil) was selected as an example to investigate the adsorption characteristic of phosphorus onto soil with the Langmuir, Freundlich, and Redlich-Peterson isotherms by both the linear and non-linear regression methods. The adsorption experiment was conducted at the temperatures of 283, 288, 298, and 308 K, respectively, to choose the appropriate method and obtain the credible adsorption parameters for soil adsorption equilibrium studies. The results showed that the non-linear regression method would be a better way to compare the better fit of isotherms for the adsorption of phosphorus onto laterite. Both the two-parameter Freundlich and the three-parameter Redlich-Peterson isotherms had higher coefficients of determination for the adsorption of phosphorus onto laterite at various temperatures. In addition, a relationship between Freundlich isotherm parameters and Redlich-Peterson isotherm parameters was presented.

Author Keywords: Adsorption, Isotherm, Non-Linear Regression, Soil, Temperature

Keywords Plus: Constructed Wetlands, Sorption Isotherm, Aqueous-Solution, Removal, Lead

Reprint Address: Ho, YS (reprint author), Asia Univ, Water Res Ctr, Taichung 41354, Taiwan

Addresses:

1. Asia Univ, Water Res Ctr, Taichung 41354, Taiwan

2. Peking Univ, Dept Environm Sci, Minist Educ, Key Lab Water & Sediment Sci, Beijing, Peoples R China

3. Wuhan Univ, Sch Resource & Environm Sci, Wuhan 430079, Peoples R China

4. Chinese Acad Sci, Inst Geodesy & Geophys, Wuhan 430077, Peoples R China

E-mail Addresses: ysho@asia.edu.tw

- Zhang, L., Wu, W.T., Liu, J.Y., Zhou, Q., Luo, J.H., Zhang, J.Q. and Wang, X.Z. (2014), Removal of phosphate from water using raw and activated laterite: batch and column studies. Desalination and Water Treatment, 52 (4-6), 775-783.

- Yoon, S.Y., Lee, C.G., Park, J.A., Kim, J.H., Kim, S.B., Lee, S.H. and Choi, J.W. (2014), Kinetic, equilibrium and thermodynamic studies for phosphate adsorption to magnetic iron oxide nanoparticles. Chemical Engineering Journal, 236), 341-347.

- Maiti, A., Thakur, B.K., Basu, J.K. and De, S. (2013), Comparison of treated laterite as arsenic adsorbent from different locations and performance of best filter under field conditions. Journal of Hazardous Materials, 262), 1176-1186.

- Jia, C.R., Dai, Y.R., Chang, J.J., Wu, C.Y., Wu, Z.B. and Liang, W. (2013), Adsorption characteristics of used brick for phosphorus removal from phosphate solution. Desalination and Water Treatment, 51 (28-30), 5886-5891.

- Zhuo, L., Ren, J.M., Wei, X.Y., Long, L.J., Chen, S.M. and Yu, C.L. (2013), Equilibrium Modeling, Kinetic and Thermodynamic Studies on the Adsorption of Methylene Blue Dye by Low-Cost Walnut Shell Power. Fresenius Environmental Bulletin, 22 (12B), 3743-3750.

- Hadi, M., Mckay, G., Samarghandi, M.R., Maleki, A. and Aminabad, M.S. (2012), Prediction of optimum adsorption isotherm: comparison of chi-square and Log-likelihood statistics. Desalination and Water Treatment, 49 (1-3), 81-94.