Last data updates: 29 March 2013

Ho, Y.S. and Ofomaja, A.E. (2005), Effects of calcium competition on lead sorption by palm kernel fibre. Journal of Hazardous Materials, 120 (1-3), 157-162.

| Document type: Article | Language: English | Cited references: 26 | Times cited: 13 | Times self cited: 3 |
| --- | --- | --- | --- | --- |

Abstract: The kinetics of sorption of a mono-solute of lead ions and of a bi-solute of lead and calcium ions onto palm kernel fibre was investigated in a batch system. The experimental data were analysed based on an intraparticle diffusion equation and a pseudo-second-order mechanism, in both the mono- and bi-solute sorption systems, in order to predict the rate constant of sorption, the equilibrium capacity, and the initial sorption rate. The results indicate that the sorption mechanism is described by a pseudo-second-order equation. Intraparticle diffusion was significant in the lower-concentration systems. In addition, a modified intraparticle diffusion equation was applied to the sorption systems. (c) 2005 Elsevier B.V. All fights reserved.

Author Keywords: Adsorption; Lead; Palm Kernel Fibre; Kinetics; Intraparticle Diffusion

KeyWords Plus: Divalent Metal-Ions; Aqueous-Solution; Removal; Peat; Adsorption; Dye; Adsorbents; Pb(II); Biosorption; Kinetics

Addresses: Ho YS (reprint author), Taipei Med Univ, Sch Publ Hlth, 250 Wu Hsing St, Taipei, 11014 Taiwan

Taipei Med Univ, Sch Publ Hlth, Taipei, 11014 Taiwan

Univ Benin, Fac Sci, Dept Chem, Benin, Edo State Nigeria

E-mail Addresses: ysho@tmu.edu.tw

- El-Sayed, G.O. (2011), Removal of methylene blue and crystal violet from aqueous solutions by palm kernel fiber. Desalination, 272 (1-3), 225-232.

- Meski, S., Ziani, S., Khireddine, H., Yataghane, F. and Ferguene, N. (2011), Elaboration of the hydroxyapatite with different precursors and application for the retention of the lead. Water Science and Technology, 63 (10), 2087-2096.

- Ahmad, T., Rafatullah, M., Ghazali, A., Sulaiman, O. and Hashim, R. (2011), Oil palm biomass-based adsorbents for the removal of water pollutants: A review. Journal of Environmental Science and Health Part C-Environmental Carcinogenesis & Ecotoxicology Reviews, 29 (3), 177-222.

- Ofomaja, A.E. (2010), Intraparticle diffusion process for lead(II) biosorption onto mansonia wood sawdust. Bioresource Technology, 101 (15), 5868-5876.

- Kolodynska, D. (2010), Diphonix Resin (R) in sorption of heavy metal ions in the presence of the biodegradable complexing agents of a new generation. Chemical Engineering Journal, 159 (1-3), 27-36.

- Ofomaja, A.E., Naidoo, E.B. and Modise, S.J. (2009), Removal of copper(II) from aqueous solution by pine and base modified pine cone powder as biosorbent. Journal of Hazardous Materials, 168 (2-3), 909-917.

- Cherifi, H., Hanini, S. and Bentahar, F. (2009), Adsorption of phenol from wastewater using vegetal cords as a new adsorbent. Desalination, 244 (1-3), 177-187.

- Ozcan, A.S., Tunali, S., Akar, T. and Ozcan, A. (2009), Biosorption of lead(II) ions onto waste biomass of Phaseolus vulgaris L.: estimation of the equilibrium, kinetic and thermodynamic parameters. Desalination, 244 (1-3), 188-198.

- Oladoja, N.A. and Akinlabi, A.K. (2009), Congo Red Biosorption on Palm Kernel Seed Coat. Industrial & Engineering Chemistry Research, 48 (13), 6188-6196.

- Dikici, H. (2009), Adsorption of Divalent Metal Ions on a Herbaceous Peat. Asian Journal of Chemistry, 21 (5), 3334-3342.

- Khan, E., Huang, C.P. and Reed, B.E. (2006), Hazardous waste treatment technologies. Water Environment Research, 78 (10), 1809-1855.

- Ho, Y.S. and Ofomaja, A.E. (2006), Kinetic studies of copper ion adsorption on palm kernel fibre. Journal of Hazardous Materials, 137 (3), 1796-1802.

- Machida, M., Yamazaki, R., Aikawa, M. and Tatsumoto, H. (2005), Role of minerals in carbonaceous adsorbents for removal of Pb(II) ions from aqueous solution. Separation and Purification Technology, 46 (1-2), 88-94.