Last data updates: 15 January 2015

Ho, Y.S. (2006), Isotherms for the sorption of lead onto peat: Comparison of linear and non-linear methods. Polish Journal of Environmental Studies, 15 (1), 81-86.

| Document type: Article | Language: English | Cited references: 11 | Times cited: 106 | Times self cited: 9 |
| --- | --- | --- | --- | --- |

Abstract: A comparison of the linear least-squares method and a trial-and-error non-linear method of three widely used isotherms (the Langmuir, Freundlich, and Redlich-Peterson) were examined in an experiment using lead ion sorption onto peat at different temperatures. The four Langmuir linear equations are discussed. Langmuir isotherm parameters obtained from the four Langmuir linear equations using the linear method differed but they were the same when using the non-linear method. Langmuir-1 is the most popular linear form, and it had the highest coefficient of determination compared with the other Langmuir linear equations. The Redlich-Peterson and Langmuir isotherms produced higher coefficients of determination. There are two separate regions depicting the Freundlich isotherm. The results show that that non-linear method may be a better way to obtain the parameters.

Author Keywords: Peat; Adsorption; Temperature; Isotherm; Lead

KeyWords Plus: Adsorption; Removal; Copper; Nickel

Addresses: Ho YS (reprint author), Peking Univ, Coll Environm Sci, Dept Environm Sci, Beijing, 100871 Peoples R China

Peking Univ, Coll Environm Sci, Dept Environm Sci, Beijing, 100871 Peoples R China

E-mail Addresses: dr_ysho@hotmail.com

- Momcilovic, M.Z., Randelovic, M.S., Purenovic, M., Onjia, A.E., Babic, B.M. and Matovic, B.Z. (2014), Synthesis and characterization of resorcinol formaldehyde carbon cryogel as efficient sorbent for imidacloprid removal. Desalination and Water Treatment, 52 (37-39), 7306-7316.

- Tabaraki, R. and Nateghi, A. (2014), Multimetal biosorption modeling of Zn2+, Cu2+ and Ni2+ by Sargassum ilicifolium. Ecological Engineering, 71), 197-205.

- Cui, L.M., Xu, W.Y., Guo, X.Y., Zhang, Y.K., Wei, Q. and Du, B. (2014), Synthesis of strontium hydroxyapatite embedding ferroferric oxide nano-composite and its application in Pb2+ adsorption. Journal of Molecular Liquids, 197), 40-47.

- Ebrahimian, A., Saberikhah, E., Emami, M.S. and Sotudeh, M. (2014), Study of Biosorption Parameters: Isotherm, Kinetics and Thermodynamics of Basic Blue 9 Biosorption Onto Foumanat Tea Waste. Cellulose Chemistry and Technology, 48 (7-8), 735-743.

- Pavlovic, M.D., Buntic, A.V., Mihajlovski, K.R., Siler-Marinkovic, S.S., Antonovic, D.G., Radovanovic, Z. and mitrijevic-Brankovic, S.I. (2014), Rapid cationic dye adsorption on polyphenol-extracted coffee grounds-A response surface methodology approach. Journal of the Taiwan Institute of Chemical Engineers, 45 (4), 1691-1699.

- Albadarin, A.B., Yang, Z.Y., Mangwandi, C., Glocheux, Y., Walker, G. and Ahmad, M.N.M. (2014), Experimental design and batch experiments for optimization of Cr(VI) removal from aqueous solutions by hydrous cerium oxide nanoparticles. Chemical Engineering Research & Design, 92 (7), 1354-1362.

- Rangabhashiyam, S., Anu, N., Nangagopal, M.S.G. and Selvaraju, N. (2014), A Novel approach of the modified BET Isotherm towards continuous column study. Journal of Scientific & Industrial Research, 73 (7), 489-494.

- Guru, P.S. and Dash, S. (2014), Sorption on eggshell waste-A review on ultrastructure, biomineralization and other applications. Advances in Colloid and Interface Science, 209), 49-67.

- Shamsizadeh, A., Ghaedi, M., Ansari, A., Azizian, S. and Purkait, M.K. (2014), Tin oxide nanoparticle loaded on activated carbon as new adsorbent for efficient removal of malachite green-oxalate: Non-linear kinetics and isotherm study. Journal of Molecular Liquids,  195), 212-218.

- Cheng, L.C., Wu, T.S., Wang, J.W., Wu, S.H., Chung, M.H., Kuo, Y.M. and Tsai, C.H. (2014), Production and Isolation of Chitosan from Aspergillus terreus and Application in Tin(II) Adsorption. Journal of Applied Polymer Science, 131 (12.

- Liang, J.L., Zhao, L.X., Du, N., Li, H.P. and Hou, W.G. (2014), Solid effect in solvent extraction treatment of pre-treated oily sludge. Separation and Purification Technology, 130), 28-33.

- Kiani, G. and Soltanzadeh, M. (2014), High capacity removal of silver(I) and lead(II) ions by modified polyacrylonitrile from aqueous solutions. Desalination and Water Treatment, 52 (16-18), 3206-3218.

- Kiani, G. (2014), High removal capacity of silver ions from aqueous solution onto Halloysite nanotubes. Applied Clay Science, 90), 159-164.

- Liu, J., Li, W.Y., Liu, Y.G., Zeng, Q.H. and Hong, S. (2014), Titanium(IV) hydrate based on chitosan template for defluoridation from aqueous solution. Applied Surface Science, 293), 46-54.

- Pal, S., Mukherjee, S. and Ghosh, S. (2014), Nonlinear kinetic analysis of phenol adsorption onto peat soil. Environmental Earth Sciences, 71 (4), 1593-1603.

- Cheng, C., Wang, J.N., Yang, X., Li, A.M. and Philippe, C. (2014), Adsorption of Ni(II) and Cd(II) from water by novel chelating sponge and the effect of alkali-earth metal ions on the adsorption. Journal of Hazardous Materials, 264), 332-341.

- Javadian, H. and Taghavi, M. (2014), Application of novel Polypyrrole/thiol-functionalized zeolite Beta/MCM-41 type mesoporous silica nanocomposite for adsorption of Hg2+ from aqueous solution and industrial wastewater: Kinetic, isotherm and thermodynamic studies. Applied Surface Science, 289), 487-494.

- vila-Jimenez, M.M., Elizade-Gonzalez, M.P., Garcia-Diaz, E., Gonzalez-Perea, M. and Guevara-Villa, M.R.G. (2014), Using Akaike Information Criterion to Select the Optimal Isotherm Equation for Adsorption from Solution. Adsorption Science & Technology, 32 (7), 605-622.

- Soto-Rios, P.C., Nakano, K., Fujibayashi, M., Leon-Romero, M. and Nishimura, O. (2014), Lead removal efficiency using biosorbents as alternative materials for permeable reactive barriers. Water Science and Technology, 70 (2), 307-314.

- Rasalingam, S., Peng, R. and Koodali, R.T. (2014), Removal of Hazardous Pollutants from Wastewaters: Applications of TiO2-SiO2 Mixed Oxide Materials. Journal of Nanomaterials, .

- Panteleimonov, A., Tkachenko, O., Baraban, A., Benvenutti, E.V., Gushikem, Y. and Kholin, Y. (2014), Probing Silica-Organic Hybrid Materials Using Small Probes: Simulation of Adsorption Equilibria Influenced by Cooperativity Effects. Adsorption Science & Technology, 32 (4), 305-320.

- Buntic, A., Pavlovic, M., Mihajlovski, K., Randjelovic, M., Rajic, N., Antonovic, D., Siler-Marinkovic, S. and mitrijevic-Brankovic, S. (2014), Removal of a Cationic Dye from Aqueous Solution by Microwave Activated Clinoptilolite-Response Surface Methodology Approach. Water Air and Soil Pollution, 225 (1.

- Rasalingam, S., Peng, R. and Koodali, R.T. (2013), An investigation into the effect of porosities on the adsorption of rhodamine B using titania-silica mixed oxide xerogels. Journal of Environmental Management, 128), 530-539.

- Mourabet, M., El Rhilassi, A., nani-Ziatni, M., El Hamri, R. and Taitai, A. (2013), Studies on fluoride adsorption by apatitic tricalcium phosphate (ATCP) from aqueous solution. Desalination and Water Treatment, 51 (34-36), 6743-6754.

- Leiviska, T., Sarpola, A., Heikkinen, E. and Tanskanen, J. (2013), Thermal properties and phosphate adsorption efficiency of coarse aluminum silicate fraction. Desalination and Water Treatment, 51 (34-36), 6837-6845.

- Kibombo, H.S., Rasalingam, S. and Koodali, R.T. (2013), Facile template free method for textural property modulation that enhances adsorption and photocatalytic activity of aperiodic titania supported silica materials. Applied Catalysis B-Environmental, 142), 119-128.

- Ghaedi, M., Ansari, A. and Sahraei, R. (2013), ZnS:Cu nanoparticles loaded on activated carbon as novel adsorbent for kinetic, thermodynamic and isotherm studies of Reactive Orange 12 and Direct yellow 12 adsorption. Spectrochimica Acta Part A-Molecular and Biomolecular Spectroscopy, 114), 687-694.

- Peng, S., Zeng, Q.H., Guo, Y.C., Niu, B.B., Zhang, X. and Hong, S. (2013), Defluoridation from aqueous solution by chitosan modified natural zeolite. Journal of Chemical Technology and Biotechnology, 88 (9), 1707-1714.

- Adhikari, B.B., Gurung, M., Alam, S., Tolnai, B. and Inoue, K. (2013), Kraft mill lignin - A potential source of bio-adsorbents for gold recovery from acidic chloride solution. Chemical Engineering Journal, 231), 190-197.

- Ebrahimian, A. and Saberikhah, E. (2013), Biosorption of Methylene Blue Onto Foumanat Tea Waste: Equilibrium and Thermodynamic Studies. Cellulose Chemistry and Technology, 47 (7-8), 657-666.

- Romero-Guzman, E.T., Reyes-Gutierrez, L.R., Marin-Allende, M.J., Gonzalez-Acevedo, Z.I. and Olguin-Gutierrez, M.T. (2013), Physicochemical properties of non-living water hyacinth (Eichhornia crassipes) and lesser duckweed (Lemna minor) and their influence on the As(V) adsorption processes. Chemistry and Ecology, 29 (5), 459-475.

- Ma, H.Y., Hsiao, B.S. and Chu, B. (2013), Electrospun Nanofibrous Membrane for Heavy Metal Ion Adsorption. Current Organic Chemistry, 17 (13), 1361-1370.

- Panahi, H.A., Karimi, M., Adinehlo, H., Nezhati, M.N., Moniri, E., Kelahrodi, S.R., Manoochehri, M., Azizi, Z. and Feizbakhsh, A. (2013), Uptake of lead(II) from water sample by 2-allyl-phenol-functionalized amberlite XAD-4: isotherm and thermodynamic study. Desalination and Water Treatment, 51 (16-18), 3114-3124.

- Kaya, E.M.O., Ozcan, A.S., Gok, O. and Ozcan, A. (2013), Adsorption kinetics and isotherm parameters of naphthalene onto natural- and chemically modified bentonite from aqueous solutions. Adsorption-Journal of the International Adsorption Society, 19 (2-4), 879-888.

- Guerra, D.J.L., Mello, I., Resende, R. and Silva, R.A.S. (2013), Kinetics and thermodynamics of Cr(VI) ion adsorption onto organo-bentonite from the Amazon region. Reaction Kinetics Mechanisms and Catalysis, 108 (2), 317-339.

- Wang, J.N., Cheng, C., Yang, X., Chen, C. and Li, A.M. (2013), A New Porous Chelating Fiber: Preparation, Characterization, and Adsorption Behavior of Pb(II). Industrial & Engineering Chemistry Research, 52 (11), 4072-4082.

- Manoochehri, M. and Amooei, K. (2013), Removal of Methylene Blue by Modified Carbon Prepared from the Sambucus Nigra L. plant. Carbon Letters, 14 (1), 27-33.

- Zhuo, L., Ren, J.M., Wei, X.Y., Long, L.J., Chen, S.M. and Yu, C.L. (2013), Equilibrium Modeling, Kinetic and Thermodynamic Studies on the Adsorption of Methylene Blue Dye by Low-Cost Walnut Shell Power. Fresenius Environmental Bulletin, 22 (12B), 3743-3750.

- Borkowski, A., Rydelek, P. and Szala, M. (2013), Adsorption studies of azotetrazolate and 3,6-dihydrazinotetrazine on peat. Journal of Environmental Science and Health Part A-Toxic/Hazardous Substances & Environmental Engineering, 48 (8), 905-911.

- bu Samah, R., Zainol, N., Yee, P.L., Pawing, C.M. and bd-Aziz, S. (2013), Adsorption of Vanillin using Macroporous Resin H103. Adsorption Science & Technology, 31 (7), 599-610.

- Dela Cruz, M.L., Arano, K., Dela Pena, E.M. and Diaz, L.J. (2013), Nanoclay-supported Zero-valent Iron as an Efficient Adsorbent Material for Arsenic. Green Technologies for Sustainable & Innovation in Materials, 686), 296-304.

- Melichova, Z. and Hromada, L. (2013), Adsorption of Pb2+ and Cu2+ Ions from Aqueous Solutions on Natural Bentonite. Polish Journal of Environmental Studies, 22 (2), 457-464.

- Sipus, I., Strkalj, A. and Glavas, Z. (2012), Removal of Cr(VI) ions from aqueous solution using foundry waste material: Kinetic and equilibrium studies. Canadian Metallurgical Quarterly, 51 (4), 413-418.

- Doskocil, L. and Pekar, M. (2012), Removal of metal ions from multi-component mixture using natural lignite. Fuel Processing Technology, 101), 29-34.

- Anirudhan, T.S., Bringle, C.D. and Radhakrishnan, P.G. (2012), Heavy metal interactions with phosphatic clay: Kinetic and equilibrium studies. Chemical Engineering Journal, 200), 149-157.

- Apopei, D.F., Dinu, M.V., Trochimczuk, A.W. and Dragan, E.S. (2012), Sorption Isotherms of Heavy Metal Ions onto Semi-Interpenetrating Polymer Network Cryogels Based on Polyacrylamide and Anionically Modified Potato Starch. Industrial & Engineering Chemistry Research, 51 (31), 10462-10471.

- Brdar, M.M., Takaci, A.A., Sciban, M.B. and Rakic, D.Z. (2012), Isotherms for the adsorption of Cu(II) onto lignin - comparison of linear and non-linear methods. Hemijska Industrija, 66 (4), 495-501.

- Sinha, A., Pant, K.K. and Khare, S.K. (2012), Studies on mercury bioremediation by alginate immobilized mercury tolerant Bacillus cereus cells. International Biodeterioration & Biodegradation, 71), 1-8.

- Wang, J.N., Xu, L., Cheng, C., Meng, Y. and Li, A.M. (2012), Preparation of new chelating fiber with waste PET as adsorbent for fast removal of Cu2+ and Ni2+ from water: Kinetic and equilibrium adsorption studies.  Chemical Engineering Journal, 193), 31-38.

- Ghasemi, Z., Seif, A., Ahmadi, T.S., Zargar, B., Rashidi, F. and Rouzbahani, G.M. (2012), Thermodynamic and kinetic studies for the adsorption of Hg(II) by nano-TiO2 from aqueous solution. Advanced Powder Technology, 23 (2), 148-156.

- Brdar, M., Sciban, M., Takaci, A. and Dosenovic, T. (2012), Comparison of two and three parameters adsorption isotherm for Cr(VI) onto Kraft lignin. Chemical Engineering Journal, 183), 108-111.

- Singh, V., Kumar, P. and Sanghi, R. (2012), Use of microwave irradiation in the grafting modification of the polysaccharides - A review. Progress in Polymer Science, 37 (2), 340-364.

- Murithi, G., Onindo, C.O. and Muthakia, G.K. (2012), Kinetic and Equilibrium Study for the Sorption of Pb(Ii) Ions from Aqueous Phase by Water Hyacinth (Eichhornia Crassipes). Bulletin of the Chemical Society of Ethiopia, 26 (2), 181-193.

- Chuang, K.Y., Olaiya, M.T. and Ho, Y.S. (2012), Bibliometric Analysis of the Polish Journal of Environmental Studies (2000-11). Polish Journal of Environmental Studies, 21 (5), 1175-1183.

- Correa-Murrieta, M.A., Lopez-Cervantes, J., Sanchez-Machado, D.I., Sanchez-Duarte, R.G., Rodriguez-Nunez, J.R. and Nunez-Gastelum, J.A. (2012), Fe(II) and Fe(III) adsorption by chitosan-tripolyphosphate beads: kinetic and equilibrium studies. Journal of Water Supply Research and Technology-Aqua, 61 (6), 331-341.

- Ghadiri, S.K., Nabizadeh, R., Mahvi, A.H., Nasseri, S., Mesdaghinia, A.R. and Talebi, S.S. (2012), Potential of granulated modified nanozeolites Y for MTBE removal from aqueous solutions: Kinetic and isotherm studies. Polish Journal of Chemical Technology, 14 (2), 1-8.

- Dogan, H. (2012), Preparation and characterization of calcium alginate-based composite adsorbents for the removal of Cd, Hg, and Pb ions from aqueous solution. Toxicological and Environmental Chemistry , 94 (3), 482-499.

- Rout, K., Mohapatra, M. and Anand, S. (2012), 2-Line ferrihydrite: synthesis, characterization and its adsorption behaviour for removal of Pb(II), Cd(II), Cu(II) and Zn(II) from aqueous solutions. Dalton Transactions, 41 (11), 3302-3312.

- Ignatowicz, K. (2011), A mass transfer model for the adsorption of pesticide on coconut shell based activated carbon. International Journal of Heat and Mass Transfer, 54 (23-24), 4931-4938.

- Dancu, A.C., Barabas, R. and Bogya, E.S. (2011), Adsorption of nicotinic acid on the surface of nanosized hydroxyapatite and structurally modified hydroxyapatite. Central European Journal of Chemistry, 9 (4), 660-669.

- Paulino, A.T., Belfiore, L.A., Kubota, L.T., Muniz, E.C., Almeida, V.C. and Tambourgi, E.B. (2011), Effect of magnetite on the adsorption behavior of Pb(II), Cd(II), and Cu(II) in chitosan-based hydrogels. Desalination, 275 (1-3), 187-196.

- Boudrahem, F., issani-Benissad, F. and Soualah, A. (2011), Adsorption of Lead(II) from Aqueous Solution by Using Leaves of Date Trees As an Adsorbent. Journal of Chemical and Engineering Data, 56 (5), 1804-1812.

- Chabani, M., Akhrib, K., Ouaissa, Y.A., Amrane, A. and Bensmaili, A. (2011), Ion-Exchange Equilibria of Nitrates on a Strongly Basic Resin. Chemical Engineering & Technology, 34 (5), 797-802.

- Bajpai, S.K. and Shrivastava, S. (2011), Sorptive Removal of Methylene Blue from Aqueous Solutions by Polymer/Activated Charcoal Composites. Journal of Applied Polymer Science, 119 (5), 2525-2532.

- Ofomaja, A.E. (2011), Kinetics and pseudo-isotherm studies of 4-nitrophenol adsorption onto mansonia wood sawdust. Industrial Crops and Products, 33 (2), 418-428.

- Chowdhury, S., Misra, R., Kushwaha, P. and Das, P. (2011), Optimum Sorption Isotherm by Linear and Nonlinear Methods for Safranin onto Alkali-Treated Rice Husk. Bioremediation Journal, 15 (2), 77-89.

- Zhang, L.A., Hong, S., He, J., Gan, F.X. and Ho, Y.S. (2011), Adsorption characteristic studies of phosphorus onto laterite. Desalination and Water Treatment, 25 (1-3), 98-105.

- Dridi-Dhaouadi, S., Ben Douissa-Lazreg, N. and M'Henni, M.F. (2011), Removal of lead and Yellow 44 acid dye in single and binary component systems by raw Posidonia oceanica and the cellulose extracted from the raw biomass. Environmental Technology, 32 (3), 325-340.

- Santos, R.R., Vermeulen, S., Haritova, A. and Fink-Gremmels, J. (2011), Isotherm modeling of organic activated bentonite and humic acid polymer used as mycotoxin adsorbents. Food Additives and Contaminants Part A-Chemistry Analysis Control Exposure & Risk Assessment, 28 (11), 1578-1589.

- Malarvizhi, R. and Ho, Y.S. (2010), The influence of pH and the structure of the dye molecules on adsorption isotherm modeling using activated carbon. Desalination, 264 (1-2), 97-101.

- Bagheri, B., Abdouss, M., Aslzadeh, M.M. and Shoushtari, A.M. (2010), Efficient Removal of Cr3+, Pb2+ and Hg2+ Ions from Industrial Effluents by Hydrolyzed/Thioamidated Polyacrylonitrile Fibres. Iranian Polymer Journal, 19 (12), 911-925.

- Alemayehu, E. and Lennartz, B. (2010), Adsorptive removal of nickel from water using volcanic rocks. Applied Geochemistry , 25 (10), 1596-1602.

- Fiorentin, L.D., Trigueros, D.E.G., Modenes, A.N., Espinoza-Quinones, F.R., Pereira, N.C., Barros, S.T.D. and Santos, O.A.A. (2010), Biosorption of reactive blue 5G dye onto drying orange bagasse in batch system: Kinetic and equilibrium modeling. Chemical Engineering Journal, 163 (1-2), 68-77.

- Zhang, L.A., Hong, S., He, J., Gan, F.X. and Ho, Y.S. (2010), Isotherm Study of Phosphorus Uptake from Aqueous Solution Using Aluminum Oxide. Clean-Soil Air Water, 38 (9), 831-836.

- Mbadcam, J.K., Wouaha, G.F.T. and Gomdje, V.H. (2010), Adsorption of Ferricyanide Ion on Activated Carbon and gamma-Alumina. E-Journal of Chemistry, 7 (3), 721-726.

- Aljundi, I.H. and Khleifat, K.M. (2010), Biosorption of lead by E. coli strains expressing Vitreoscilla hemoglobin: Isotherm modeling with two- and three-parameter models. Engineering in Life Sciences, 10 (3), 225-232.

- Es'haghi, Z., Golsefidi, M.A., Saify, A., Tanha, A.A., Rezaeifar, Z. and ian-Nezhadi, Z. (2010), Carbon nanotube reinforced hollow fiber solid/liquid phase microextraction: A novel extraction technique for the measurement of caffeic acid in Echinacea purpurea herbal extracts combined with high-performance liquid chromatography. Journal of Chromatography A, 1217 (17), 2768-2775.

- Adie, D.B., Olarinoye, N.O., Oke, I.A., Ismail, A., Lukman, S. and Otun, J.A. (2010), Removal of Lead Ions from Aqueous Solutions Using Powdered Corn Cobs. Canadian Journal of Chemical Engineering, 88 (2), 241-255.

- Pandey, P.K., Sharma, S.K. and Sambi, S.S. (2010), Kinetics and equilibrium study of chromium adsorption on zeoliteNaX. International Journal of Environmental Science and Technology, 7 (2), 395-404.

- Ngah, W.S.W. and Fatinathan, S. (2010), Adsorption characterization of Pb(II) and Cu(II) ions onto chitosan-tripolyphosphate beads: Kinetic, equilibrium and thermodynamic studies. Journal of Environmental Management, 91 (4), 958-969.

- Rahman, R.O.A., Ibrahim, H.A., Hanafy, M. and Monem, N.M.A. (2010), Assessment of synthetic zeolite Na A-X as sorbing barrier for strontium in a radioactive disposal facility. Chemical Engineering Journal, 157 (1), 100-112.

- Natarajan, B. and Nagarajan, S. (2010), Utilisation of Agriculture Weed for the Removal of Cr(VI) from Aqueous Solution. Acta Chimica Slovenica, 57 (3), 693-699.

- He, J., Hong, S., Zhang, L.A., Gan, F.X. and Ho, Y.S. (2010), Equilibrium and Thermodynamic Parameters of Adsorption of Methylene Blue Onto Rectorite. Fresenius Environmental Bulletin, 19 (11A), 2651-2656.

- Ignatowicz, K. (2010), Application of Mathematical Models of Sorption Process to Describe the Removal of HCH Pesticide on Vermicompost. Rocznik Ochrona Srodowiska, 12), 525-542.

- Ismail, A., Adie, D.B., Oke, I.A., Otun, J.A., Olarinoye, N.O., Lukman, S. and Okuofu, C.A. (2009), Adsorption Kinetics of Cadmium Ions Onto Powdered Corn Cobs. Canadian Journal of Chemical Engineering , 87 (6), 896-909.

- Kushwaha, S., Sodaye, S. and Sudhakar, P.P. (2009), Adsorption of Hg(II) from aqueous solution onto Borassus Flabeliffer: equilibrium and kinetic studies. Desalination and Water Treatment, 12 (1-3), 100-107.

- Ignatowicz, K. (2009), Selection of sorbent for removing pesticides during water treatment. Journal of Hazardous Materials, 169 (1-3), 953-957.

- Hong, S., Wen, C., He, J., Gan, F.X. and Ho, Y.S. (2009), Adsorption thermodynamics of Methylene Blue onto bentonite. Journal of Hazardous Materials, 167 (1-3), 630-633.

- Chabani, M., Amrane, A. and Bensmaili, A. (2009), Equilibrium sorption isotherms for nitrate on resin Amberlite IRA 400. Journal of Hazardous Materials, 165 (1-3), 27-33.

- Zhang, J., Xie, S.D. and Ho, Y.S. (2009), Removal of fluoride ions from aqueous solution using modified attapulgite as adsorbent. Journal of Hazardous Materials, 165 (1-3), 218-222.

- Febrianto, J., Kosasih, A.N., Sunarso, J., Ju, Y.H., Indraswati, N. and Ismadji, S. (2009), Equilibrium and kinetic studies in adsorption of heavy metals using biosorbent: A summary of recent studies. Journal of Hazardous Materials, 162 (2-3), 616-645.

- Wang, X.S., Tang, Y.P. and Tao, S.R. (2008), Removal of Cr (VI) from aqueous solutions by the nonliving biomass of Alligator weed: kinetics and equilibrium. Adsorption-Journal of the International Adsorption Society, 14 (6), 823-830.

- Arief, V.O., Trilestari, K., Sunarso, J., Indraswati, N. and Ismadji, S. (2008), Recent Progress on Biosorption of Heavy Metals from Liquids Using Low Cost Biosorbents: Characterization, Biosorption Parameters and Mechanism Studies. Clean-Soil Air Water, 36 (12), 937-962.

- Ofomaja, A.E. and Ho, Y.S. (2008), Effect of temperatures and pH on methyl violet biosorption by Mansonia wood sawdust. Bioresource Technology, 99 (13), 5411-5417.

- Boulinguiez, B., Le Cloirec, P. and Wolbert, D. (2008), Revisiting tine determination of langnmir parameters - Application to tetrahydriotlhiophene adsorption onto activated carbon. Langmuir, 24 (13), 6420-6424.

- Sundaram, C.S., Viswanathan, N. and Meenakshi, S. (2008), Defluoridation chemistry of synthetic hydroxyapatite at nano scale: Equilibrium and kinetic studies. Journal of Hazardous Materials, 155 (1-2), 206-215.

- Kumar, K.V., Porkodi, K. and Rocha, F. (2008), Isotherms and thermodynamics by linear and non-linear regression analysis for the sorption of methylene blue onto activated carbon: Comparison of various error functions. Journal of Hazardous Materials, 151 (2-3), 794-804.

- Wang, X.S., He, L., Hu, H.Q. and Wang, J. (2008), Effect of temperature on the Pb(II) removal from single aqueous solutions by a locally natural mordenite: Equilibrium and kinetic modeling. Separation Science and Technology, 43 (4), 908-922.

- Kumar, K.V., Porkodi, K. and Rocha, F. (2008), Comparison of various error functions in predicting the optimum isotherm by linear and non-linear regression analysis for the sorption of basic red 9 by activated carbon. Journal of Hazardous Materials, 150 (1), 158-165.

- Ignatowicz, K. (2008), Sorption process for migration reduction of pesticides from graveyards. Archives of Environmental Protection, 34 (3), 143-149.

- Sari, A., Tuzen, M., Citak, D. and Soylak, M. (2007), Equilibrium, kinetic and thermodynamic studies of adsorption of Pb(II) from aqueous solution onto Turkish kaolinite clay. Journal of Hazardous Materials, 149 (2), 283-291.

- Karadag, D., Koc, Y., Turan, M. and Ozturk, M. (2007), A comparative study of linear and non-linear regression analysis for ammonium exchange by clinoptilolite zeolite. Journal of Hazardous Materials, 144 (1-2), 432-437.

- Ho, Y.S. and Ofomaja, A.E. (2006), Kinetic studies of copper ion adsorption on palm kernel fibre. Journal of Hazardous Materials, 137 (3), 1796-1802.