Last data updates: 12 February 2015

Ho, Y.S., Huang, C.T. and Huang, H.W. (2002), Equilibrium sorption isotherm for metal ions on tree fern. Process Biochemistry, 37 (12), 1421-1430.

| Document type: Article | Language: English | Cited References: 25 | Times Cited: 263 | Times self cited: 18 |
| --- | --- | --- | --- | --- |

Abstract: A new sorbent system for removing heavy metal ions, such as Zn(II), Cu(II) and Pb(II), from aqueous solutions has been investigated. This new sorbent is tree fern, an agriculture product. Variables of the system include solution temperature and sorbent particle size. The experimental results were fitted to the Langmuir, Freundlich and Redlich-Peterson isotherms to obtain the characteristic parameters of each model. Both the Langmuir and Redlich-/Peterson isotherms were found to well represent the measured sorption data. According to the evaluation using the Langmuir equation, the maximum sorption capacities of metal ions onto tree fern were 7.58 mg/g for Zn(II), 10.6 mg/g for Cu(II) and 39.8 mg/g for Pb(II). It was noted that an increase in temperature resulted in a higher metal loading per unit weight of the sorbent. Decreasing the particle sizes of tree fern led in an increase in the metal uptake per unit weight of the sorbent. # 2002 Elsevier Science Ltd. All rights reserved.

Keywords: Agriculture Product, Sorption, Copper, Zinc, Lead, Tree Fern, Aqueous-Solutions, Heavy-Metals, Removal, Adsorption, Adsorbents, Cadmium, Cations, Copper, Water, Acid

Addresses: Ho YS (reprint author), Taipei Med Univ, Sch Publ Hlth, 250 Wu Hsing St, Taipei, Taiwan

Taipei Med Univ, Sch Publ Hlth, Taipei, Taiwan

- Sui, N., Wang, L.N., Wu, X.H., Li, X.H., Sui, J., Xiao, H.L., Liu, M.H., Wan, J. and Yu, W.W. (2015), Polyethylenimine modified magnetic graphene oxide nanocomposites for Cu2+ removal. Rsc Advances, 5 (1), 746-752.

- Waseem, S., Din, M.I., Nasir, S. and Rasool, A. (2014), Evaluation of Acacia nilotica as a non conventional low cost biosorbent for the elimination of Pb(II) and Cd(II) ions from aqueous solutions. Arabian Journal of Chemistry, 7 (6), 1091-1098.

- Baig, S.A., Zhu, J., Muhammad, N., Sheng, T.T. and Xu, X.H. (2014), Effect of synthesis methods on magnetic Kans grass biochar for enhanced As(III, V) adsorption from aqueous solutions. Biomass & Bioenergy, 71), 299-310.

- Dwivedi, A.D., Dubey, S.P., Hokkanen, S., Fallah, R.N. and Sillanpaa, M. (2014), Recovery of gold from aqueous solutions by taurine modified cellulose: An adsorptive-reduction pathway. Chemical Engineering Journal, 255), 97-106.

- Santra, D., Joarder, R. and Sarkar, M. (2014), Taguchi design and equilibrium modeling for fluoride adsorption on cerium loaded cellulose nanocomposite bead. Carbohydrate Polymers, 111), 813-821.

- Dwivedi, A.D., Dubey, S.P., Hokkanen, S. and Sillanpaa, M. (2014), Mechanistic investigation on the green recovery of ionic, nanocrystalline, and metallic gold by two anionic nanocelluloses. Chemical Engineering Journal, 253), 316-324.

- Wu, Q., You, R.R., Clark, M. and Yu, Y. (2014), Pb(II) removal from aqueous solution by a low-cost adsorbent dry desulfurization slag. Applied Surface Science, 314), 129-137.

- Chandramouleeswaran, S. and Ramkumar, J. (2014), n-Benzoyl-n-phenylhydroxylamine impregnated Amberlite XAD-4 beads for selective removal of thorium. Journal of Hazardous Materials, 280), 514-523.

- Niad, M., Rasoolzadeh, L. and Zarei, F. (2014), Biosorption of copper (II) on Sargassum angostifolium C.Agardh phaeophyceae biomass. Chemical Speciation and Bioavailability, 26 (3), 176-183.

- Singh, T. and Singhal, R. (2014), Regenerable hydrogels based on poly(acrylic acid-sodium acrylate-acrylamide) modified by sodium humate for high removal of Pb2+ and Fe2+ ions: metal adsorption kinetics and thermodynamic studies. Desalination and Water Treatment, 52 (28-30), 5611-5628.

- Lu, H.Y., Yang, L.Z., Shabbir, S. and Wu, Y.H. (2014), The adsorption process during inorganic phosphorus removal by cultured periphyton. Environmental Science and Pollution Research, 21 (14), 8782-8791.

- Baig, S.A., Sheng, T.T., Sun, C., Xue, X.Q., Tan, L.S. and Xu, X.H. (2014), Arsenic Removal from Aqueous Solutions Using Fe3O4-HBC Composite: Effect of Calcination on Adsorbents Performance. Plos One, 9 (6.

- Kumari, S. and Chauhan, G.S. (2014), New Cellulose-Lysine Schiff-Base-Based Sensor-Adsorbent for Mercury Ions. Acs Applied Materials & Interfaces, 6 (8), 5908-5917.

- Reddy, K.R., Xie, T. and Dastgheibi, S. (2014), Adsorption of mixtures of nutrients and heavy metals in simulated urban stormwater by different filter materials. Journal of Environmental Science and Health Part A-Toxic/Hazardous Substances & Environmental Engineering, 49 (5), 524-539.

- Jaafarzadeh, N., Teymouri, P., Babaei, A.A., Alavi, N. and Ahmadi, M. (2014), Biosorption of Cadmium (Ii) from Aqueous Solution by Nacl-Treated Ceratophyllum Demersum. Environmental Engineering and Management Journal, 13 (4), 763-773.

- Lee, W.C., Kim, S.O., Ranville, J., Yun, S.T. and Choi, S.H. (2014), Sequestration of arsenate from aqueous solution using 2-line ferrihydrite: equilibria, kinetics, and X-ray absorption spectroscopic analysis. Environmental Earth Sciences, 71 (8), 3307-3318.

- Belala, Z., Mechati, F., Jeguirim, M., Belhachemi, M. and Addoun, F. (2014), Equilibrium Modelling of Copper Ions Biosorption by Date Stones and Palm-Trees Waste. Environmental Engineering and Management Journal, 13 (3), 653-662.

- Sadeghalvad, B., Armaghan, M. and Azadmehr, A. (2014), Using Iranian Bentonite (Birjand Area) to Remove Cadmium from Aqueous Solutions. Mine Water and the Environment, 33 (1), 79-88.

- Liu, Y., Kang, Y.R., Mu, B. and Wang, A.Q. (2014), Attapulgite/bentonite interactions for methylene blue adsorption characteristics from aqueous solution. Chemical Engineering Journal, 237), 403-410.

- Kim, S.O., Lee, W.C., Cho, H.G., Lee, B.T., Lee, P.K. and Choi, S.H. (2014), Equilibria, kinetics, and spectroscopic analyses on the uptake of aqueous arsenite by two-line ferrihydrite. Environmental Technology, 35 (3), 251-261.

- Rajesh, Y., Pujari, M. and Uppaluri, R. (2014), Equilibrium and Kinetic Studies of Ni (II) Adsorption using Pineapple and Bamboo Stem Based Adsorbents. Separation Science and Technology, 49 (4), 533-544.

- Hossain, M.A., Ngo, H.H., Guo, W.S., Nguyen, T.V. and Vigneswaran, S. (2014), Performance of cabbage and cauliflower wastes for heavy metals removal. Desalination and Water Treatment, 52 (4-6), 844-860.

- Cheng, C., Wang, J.N., Yang, X., Li, A.M. and Philippe, C. (2014), Adsorption of Ni(II) and Cd(II) from water by novel chelating sponge and the effect of alkali-earth metal ions on the adsorption. Journal of Hazardous Materials, 264), 332-341.

- Zhao, Y.Q., Liang, H.E. and Han, C.H. (2014), Preparation of New Hydrophilic PET Fiber by Grafting with Acrylic Acid and Modification with Amino Groups for Improvement of Dyeing Ability. Textile Bioengineering and Informatics Symposium Proceedings, 2014, Vols 1 and 2, ), 89-94.

- Thilagavathy, P. and Santhi, T. (2014), Studies on the Removal of Cu(II) from Aqueous Solutions using Modified Acacia nilotica Leaf. Bioresources, 9 (3), 3805-3824.

- Varank, G., Demir, A., Bilgili, M.S., Top, S., Sekman, E., Yazici, S. and Erkan, H.S. (2014), Equilibrium and Kinetic Studies on the Removal of Heavy Metal Ions with Natural Low-Cost Adsorbents. Environment Protection Engineering, 40 (3), 43-61.

- Dubey, S.P., Dwivedi, A.D., Sillanpaa, M., Kwon, Y.N. and Lee, C. (2014), Single-step green synthesis of imine-functionalized carbon spheres and their application in uranium removal from aqueous solution. Rsc Advances, 4 (86), 46114-46121.

- Dutta, D.P., Mathur, A., Ramkumar, J. and Tyagi, A.K. (2014), Sorption of dyes and Cu(II) ions from wastewater by sonochemically synthesized MnWO4 and MnMoO4 nanostructures. Rsc Advances, 4 (70), 37027-37035.

- Ciobanu, C.S., Iconaru, S.L., Popa, C.L., Costescu, A., Motelica-Heino, M. and Predoi, D. (2014), Porous Methyltrimethoxysilane Coated Nanoscale-Hydroxyapatite for Removing Lead Ions from Aqueous Solutions. Journal of Nanomaterials, .

- Rasalingam, S., Peng, R. and Koodali, R.T. (2014), Removal of Hazardous Pollutants from Wastewaters: Applications of TiO2-SiO2 Mixed Oxide Materials. Journal of Nanomaterials, .

- Reddy, K.R., Xie, T. and Dastgheibi, S. (2014), Nutrients Removal from Urban Stormwater by Different Filter Materials. Water Air and Soil Pollution, 225 (1.

- Liu, H. and Wang, C.Y. (2014), Chitosan scaffolds for recyclable adsorption of Cu(II) ions. Rsc Advances,  4 (8), 3864-3872.

- Ozdes, D., Gundogdu, A., Kemer, B., Duran, C., Kucuk, M. and Soylak, M. (2014), Assessment of Kinetics, Thermodynamics and Equilibrium Parameters of Cr(Vi) Biosorption Onto Pinus Brutia Ten. Canadian Journal of Chemical Engineering, 92 (1), 139-147.

- Do, X.H. and Lee, B.K. (2013), Removal of Pb2+ using a biochar-alginate capsule in aqueous solution and capsule regeneration. Journal of Environmental Management, 131), 375-382.

- Park, J.H., Choppala, G., Lee, S.J., Bolan, N., Chung, J.W. and Edraki, M. (2013), Comparative Sorption of Pb and Cd by Biochars and Its Implication for Metal Immobilization in Soils. Water Air and Soil Pollution, 224 (12.

- Rasalingam, S., Peng, R. and Koodali, R.T. (2013), An investigation into the effect of porosities on the adsorption of rhodamine B using titania-silica mixed oxide xerogels. Journal of Environmental Management, 128), 530-539.

- Singh, T. and Singhal, R. (2013), Reuse of a waste adsorbent poly(AAc/AM/SH)-Cu superabsorbent hydrogel, for the potential phosphate ion removal from waste water: Matrix effects, adsorption kinetics, and thermodynamic studies. Journal of Applied Polymer Science, 129 (6), 3126-3139.

- Peng, S., Zeng, Q.H., Guo, Y.C., Niu, B.B., Zhang, X. and Hong, S. (2013), Defluoridation from aqueous solution by chitosan modified natural zeolite. Journal of Chemical Technology and Biotechnology, 88 (9), 1707-1714.

- Demir, V. and Bin-Shafique, S. (2013), Column Studies on Effect of Phosphate Immobilization on Removal of Metals from Stormwater Runoff in Bioretention Cell. Asian Journal of Chemistry,  25 (7), 3909-3912.

- Wang, K., Xing, W.H., Zhong, Z.X. and Fan, Y.Q. (2013), Study on adsorption phenomenon of diffusion dialysis for acid recovery. Separation and Purification Technology, 110), 144-149.

- Xiang, T., Fu, H., Yue, W.W., Sun, S.D. and Zhao, C.S. (2013), Preparation and Characterization of Poly(Acrylonitrile-co-Maleic Anhydride) Copolymer Modified Polyethersulfone Membranes. Separation Science and Technology, 48 (11), 1627-1635.

- Savci, S. (2013), Biosorption of Ranitidine Onto Live Activated Sludge. Asian Journal of Chemistry, 25 (6), 3175-3178.

- Li, S.L., Gu, X. and Hu, Y.Z. (2013), Adsorption Studies of Cu(II) onto Total Polysaccharide Extracted from Astragals. Asian Journal of Chemistry, 25 (5), 2857-2860.

- Huang, L.H., Shi, C.X., Zhang, B., Niu, S.F. and Gao, B.Y. (2013), Characterization of Activated Carbon Fiber by Microwave Heating and the Adsorption of Tetracycline Antibiotics. Separation Science and Technology, 48 (9), 1356-1363.

- Saber-Samandari, S. and Gazi, M. (2013), Removal of Mercury (II) from Aqueous Solution using Chitosan-graft-Polyacrylamide Semi-IPN Hydrogels. Separation Science and Technology, 48 (9), 1382-1390.

- Wang, J.N., Cheng, C., Yang, X., Chen, C. and Li, A.M. (2013), A New Porous Chelating Fiber: Preparation, Characterization, and Adsorption Behavior of Pb(II). Industrial & Engineering Chemistry Research, 52 (11), 4072-4082.

- Zafar, M.N., Wahid, A., Ghauri, M.A., Zubair, M., Mumtaz, M.W., Anwar, F. and Danish, M. (2013), Trichoderma harzianum: a green sorbent for Pb(II) uptake from aqueous solutions. Toxicological and Environmental Chemistry, 95 (3), 422-433.

- Moreno-Pirajan, J.C. and Giraldo, L. (2013), Activated carbon from bamboo waste modified with iron and its application in the study of the adsorption of arsenite and arsenate. Central European Journal of Chemistry, 11 (2), 160-170.

- Jakubus, M. (2013), Evaluation of Maturity and Stability Parameters of Composts Prepared with Sewage Sludge. Fresenius Environmental Bulletin, 22 (11A), 3398-3414.

- Demir, V. and Bin-Shafique, S. (2013), Effect of the Presence of Phosphate Based Fertilizer on Metal Removal Capacity of Native Bioretention Materials. Fresenius Environmental Bulletin,  22 (1), 123-127.

- Vieira, E.G., Soares, I.V., da Silva, N.C., Perujo, S.D., do Carmo, D.R. and Dias, N.L. (2013), Synthesis and characterization of 3-[(thiourea)-propyl]-functionalized silica gel and its application in adsorption and catalysis. New Journal of Chemistry, 37 (7), 1933-1943.

- Feroze, N., Kazmi, M., Iqbal, W. and Muhammad, S. (2013), Adsorption of Toxic Heavy Metal on Waste Tire Crumb. Journal of Environmental Protection and Ecology, 14 (1), 85-98.

- Patrulea, V., Negrulescu, A., Mincea, M.M., Pitulice, L.D., Spiridon, O.B. and Ostafea, V. (2013), Optimization of the Removal of Copper(II) Ions from Aqueous Solution on Chitosan and Cross-Linked Chitosan Beads. Bioresources, 8 (1), 1147-1165.

- Kazmi, M., Feroze, N., Javed, H., Zafar, M. and Ramzan, N. (2012), Biosorption of Copper (II) on Dry Fruit by Product: Characterization, Kinetic and Equilibrium Studies. Journal of the Chemical Society of Pakistan, 34 (6), 1356-1365.

- Wahab, M.A., Boubakri, H., Jellali, S. and Jedidi, N. (2012), Characterization of ammonium retention processes onto Cactus leaves fibers using FTIR, EDX and SEM analysis. Journal of Hazardous Materials , 241), 101-109.

- Khalfaoui, A. and Meniai, A.H. (2012), Application of chemically modified orange peels for removal of copper(II) from aqueous solutions. Theoretical Foundations of Chemical Engineering, 46 (6), 732-739.

- Wu, D.L., Wang, W., Zhang, J.H., Fu, H., Lv, X.S. and Xu, X.H. (2012), Preparation of Mulberry Branch Biomass Char and Its Usage in Wastewater Treatment. Water Environment Research, 84 (11), 2060-2069.

- Wang, X.H. and Wang, A.Q. (2012), Equilibrium isotherm and mechanism studies of Pb(II) and Cd(II) ions onto hydrogel composite based on vermiculite. Desalination and Water Treatment, 48 (1-3), 38-49.

- Hossain, M.A., Ngo, H.H., Guo, W.S. and Setiadi, T. (2012), Adsorption and desorption of copper(II) ions onto garden grass. Bioresource Technology, 121), 386-395.

- Jeon, C.S., Park, S.W., Baek, K., Yang, J.S. and Park, J.G. (2012), Application of iron-coated zeolites (ICZ) for mine drainage treatment. Korean Journal of Chemical Engineering, 29 (9), 1171-1177.

- Bhanupriya, M., Kailash, D. and Vinod, V. (2012), Comparative Study and Treatment of Copper Using Activated carbon and Poly Vinyl Alcohol coated Activated carbon as Adsorbents. Research Journal of Chemistry and Environment, 16 (3), 39-43.

- Wang, J.N., Xu, L., Cheng, C., Meng, Y. and Li, A.M. (2012), Preparation of new chelating fiber with waste PET as adsorbent for fast removal of Cu2+ and Ni2+ from water: Kinetic and equilibrium adsorption studies.  Chemical Engineering Journal, 193), 31-38.

- Ravichandran, P., Farzana, M.H. and Meenakshi, S. (2012), Sorption equilibrium and kinetic studies of Direct Yellow 12 using carbon prepared from bagasse, rice husk and textile waste cloth. Indian Journal of Chemical Technology, 19 (2), 103-110.

- Mohsen-Nia, M., Bidgoli, M.M., Behrashi, M. and Nia, A.M. (2012), Human Serum Protein Adsorption onto Synthesis Nano-Hydroxyapatite. Protein Journal, 31 (2), 150-157.

- Jakubus, M. (2012), Evaluation of Compost by Selected Chemical and Biological Methods. Fresenius Environmental Bulletin, 21 (11C), 3464-3472.

- Rao, R.A.K. and Kashifuddin, M. (2012), Adsorption Properties of Coriander Seed Powder (Coriandrum sativum): Extraction and Pre-concentration of Pb(II), Cu(II) and Zn(II) Ions from Aqueous Solution. Adsorption Science & Technology, 30 (2), 127-146.

- Ravichandran, P., Sowmya, A. and Meenakshi, S. (2012), Equilibrium and Kinetic Studies on the Removal of Basic Violet 10 from Aqueous Solutions Using Activated Carbons Prepared from Industrial Wastes. Bioremediation Journal, 16 (2), 86-96.

- Liu, Y., Wu, L.F., Zhao, X.Y. and Luo, A.Q. (2012), Synthesis and Adsorption Property of Hydrophilic Uridine Molecularly Imprinted Polymers. International Journal of Polymer Analysis and Characterization, 17 (1), 38-47.

- Gupta, A., Yunus, M. and Sankararamakrishnan, N. (2012), Zerovalent iron encapsulated chitosan nanospheres - A novel adsorbent for the removal of total inorganic Arsenic from aqueous systems. Chemosphere, 86 (2), 150-155.

- Kumar, R., Bhatia, D., Singh, R. and Bishnoi, N.R. (2012), Metal tolerance and sequestration of Ni(II), Zn(II) and Cr(VI) ions from simulated and electroplating wastewater in batch process: Kinetics and equilibrium study. International Biodeterioration & Biodegradation, 66 (1), 82-90.

- Blazquez, G., Calero, M., Hernainz, F., Tenorio, G. and Martin-Lara, M.A. (2011), Batch and continuous packed column studies of chromium (III) biosorption by olive stone. Environmental Progress & Sustainable Energy, 30 (4), 576-585.

- Huang, R.H., Wang, B., Yang, B.C., Zheng, D.S. and Zhang, Z.Q. (2011), Equilibrium, kinetic and thermodynamic studies of adsorption of Cd(II) from aqueous solution onto HACC-bentonite. Desalination, 280 (1-3), 297-304.

- Jamil, T.S., Ghafar, H.H.A., Ibrahim, H.S. and El-Maksoud, I.H.A. (2011), Removal of methylene blue by two zeolites prepared from naturally occurring Egyptian kaolin as cost effective technique. Solid State Sciences, 13 (10), 1844-1851.

- Danish, M., Hashim, R., Ibrahim, M.N.M., Rafatullah, M., Sulaiman, O., Ahmad, T., Shamsuzzoha, M. and Ahmad, A. (2011), Sorption of Copper(II) and Nickel(II) Ions from Aqueous Solutions Using Calcium Oxide Activated Date (Phoenix dactylifera) Stone Carbon: Equilibrium, Kinetic, and Thermodynamic Studies. Journal of Chemical and Engineering Data, 56 (9), 3607-3619.

- Mellouk, S., Belhakem, A., Marouf-Khelifa, K., Schott, J. and Khelifa, A. (2011), Cu(II) adsorption by halloysites intercalated with sodium acetate. Journal of Colloid and Interface Science, 360 (2), 716-724.

- Saeed, K., Park, S.Y. and Oh, T.J. (2011), Preparation of Hydrazine-Modified Polyacrylonitrile Nanofibers for the Extraction of Metal Ions from Aqueous Media. Journal of Applied Polymer Science, 121 (2), 869-873.

- Calero, M., Hernainz, F., Blazquez, G., Dionisio, E. and Martin-Lara, M.A. (2011), Evaluation of copper biosorption almond shells. Afinidad, 68 (554), 274-284.

- Farooq, U., Khan, M.A., Athar, M. and Kozinski, J.A. (2011), Effect of modification of environmentally friendly biosorbent wheat (Triticum aestivum) on the biosorptive removal of cadmium(II) ions from aqueous solution. Chemical Engineering Journal, 171 (2), 400-410.

- Liu, Y., Zheng, Y.A. and Wang, A.Q. (2011), Effect of biotite content of hydrogels on enhanced removal of methylene blue from aqueous solution. Ionics, 17 (6), 535-543.

- El-Bayaa, A.A., Badawy, N.A., Gamal, A.M., Zidan, I.H. and Mowafy, A.R. (2011), Purification of wet process phosphoric acid by decreasing iron and uranium using white silica sand. Journal of Hazardous Materials, 190 (1-3), 324-329.

- Moradi, O. (2011), The Removal of Ions by Functionalized Carbon Nanotube: Equilibrium, Isotherms and Thermodynamic Studies. Chemical and Biochemical Engineering Quarterly, 25 (2), 229-240.

- Wang, X.S. and Lin, H.Q. (2011), Adsorption of basic dyes by dried waste sludge: Kinetic, equilibrium and desorption studies. Desalination and Water Treatment, 29 (1-3), 10-19.

- Qu, R.J., Wang, M.H., Song, R.F., Sun, C.M., Zhang, Y., Sun, X.Y., Ji, C.N., Wang, C.H. and Yin, P. (2011), Adsorption Kinetics and Isotherms of Ag(I) and Hg(II) onto Silica Gel with Functional Groups of Hydroxyl- or Amino-Terminated Polyamines. Journal of Chemical and Engineering Data, 56 (5), 1982-1990.

- Dwivedi, A.D., Gopal, K. and Jain, R. (2011), Strengthening adsorption characteristics of non-steroidal anti-inflammatory drug onto microwave-assisted mesoporous material: Process design, mechanism and characterization. Chemical Engineering Journal, 168 (3), 1279-1288.

- El-Sikaily, A., El Nemr, A. and Khaled, A. (2011), Copper sorption onto dried red alga Pterocladia capillacea and its activated carbon. Chemical Engineering Journal, 168 (2), 707-714.

- Yin, Z.H., Fu, K.Y., Gao, J.A., Cao, X.L., Li, L.L. and Zhao, C.S. (2011), Preparation, Characterization, and Testing of a Composite Membrane with pH Sensitivity. Journal of Applied Polymer Science, 119 (6), 3607-3614.

- Suharso and Buhani. (2011), Biosorption of Pb(II), Cu(II) and Cd(II) from Aqueous Solution Using Cassava Peel Waste Biomass. Asian Journal of Chemistry, 23 (3), 1112-1116.

- Jang, A., Zou, Z.W., Lee, K.K., Ahn, C.H. and Bishop, P.L. (2011), State-of-the-art lab chip sensors for environmental water monitoring. Measurement Science & Technology, 22 (3.

- Malekian, R., bedi-Koupai, J., Eslamian, S.S., Mousavi, S.F., Abbaspour, K.C. and Afyuni, M. (2011), Ion-exchange process for ammonium removal and release using natural Iranian zeolite. Applied Clay Science, 51 (3), 323-329.

- Lin, X.Z., Ma, T.Y. and Yuan, Z.Y. (2011), Titania-silica-phosphonate triconstituent hybrid mesoporous materials as adsorbents in gas and liquid phases. Chemical Engineering Journal, 166 (3), 1144-1151.

- SenthilKumar, P., Sathyaselvabala, V., Selvaraj, D., Vijayalakshmi, P. and Sivanesan, S. (2011), Adsorption Equilibrium Studies on Copper (Ii) Ions Removal by Natural Waste Using Non-Linear Approach. Environmental Engineering and Management Journal, 10 (2), 285-295.

- SenthilKumar, P., Ramalingam, S., Sathyaselvabala, V., Kirupha, S.D. and Sivanesan, S. (2011), Removal of copper(II) ions from aqueous solution by adsorption using cashew nut shell. Desalination, 266 (1-3), 63-71.

- Fusova, L., Cablik, V. and Nezvalova, L. (2011), Bentonite and Its Modified Derivates As Adsorbents of Lead. 11Th International Multidisciplinary Scientific Geoconference (Sgem 2011), Vol Iii, ), 199-206.

- Hubbe, M.A., Hasan, S.H. and Ducoste, J.J. (2011), Cellulosic Substrates for Removal of Pollutants from Aqueous Systems: A Review. 1. Metals. Bioresources, 6 (2), 2161-U2914.

- Zhang, L.A., Hong, S., He, J., Gan, F.X. and Ho, Y.S. (2011), Adsorption characteristic studies of phosphorus onto laterite. Desalination and Water Treatment, 25 (1-3), 98-105.

- Mao, J.A., Kwak, I.S., Sathishkumar, M., Sneha, K. and Yun, Y.S. (2011), Preparation of PEI-coated bacterial biosorbent in water solution: Optimization of manufacturing conditions using response surface methodology. Bioresource Technology, 102 (2), 1462-1467.

- Soares, M.R., Casagrande, J.C. and Mouta, E.R. (2011), Nickel Adsorption by Variable Charge Soils: Effect of pH and Ionic Strength. Brazilian Archives of Biology and Technology, 54 (1), 207-220.

- Almeida, C.A.P., dos Santos, A., Jaerger, S., Debacher, N.A. and Hankins, N.P. (2010), Mineral waste from coal mining for removal of astrazon red dye from aqueous solutions. Desalination, 264 (3), 181-187.

- Malarvizhi, R. and Ho, Y.S. (2010), The influence of pH and the structure of the dye molecules on adsorption isotherm modeling using activated carbon. Desalination, 264 (1-2), 97-101.

- Dwivedi, A.D., Dubey, S.P., Gopal, K. and Tandon, V.K. (2010), A comparative investigation for strengthening the adsorptive phenomenon by activated natural minerals and plant waste-carbon for defluoridation in water milieu. Desalination, 263 (1-3), 189-199.

- Wahab, M.A., Jellali, S. and Jedidi, N. (2010), Effect of temperature and pH on the biosorption of ammonium onto Posidonia oceanica fibers: Equilibrium, and kinetic modeling studies. Bioresource Technology, 101 (22), 8606-8615.

- Ozsoy, H.D. and van Leeuwen, J. (2010), Removal of color from fruit candy waste by activated carbon adsorption. Journal of Food Engineering, 101 (1), 106-112.

- Hasan, S.H. and Ranjan, D. (2010), Agro-Industrial Waste: A Low-Cost Option for the Biosorptive Remediation of Selenium Anions. Industrial & Engineering Chemistry Research, 49 (19), 8927-8934.

- Liu, Y., Wang, W.B. and Wang, A.G. (2010), Adsorption of lead ions from aqueous solution by using carboxymethyl cellulose-g-poly (acrylic acid)/attapulgite hydrogel composites. Desalination, 259 (1-3), 258-264.

- Zhang, L.A., Hong, S., He, J., Gan, F.X. and Ho, Y.S. (2010), Isotherm Study of Phosphorus Uptake from Aqueous Solution Using Aluminum Oxide. Clean-Soil Air Water, 38 (9), 831-836.

- Moreno-Pirajan, J.C., Gomez-Cruz, R., Garcia-Cuello, V.S. and Giraldo, L. (2010), Binary system Cu(II)/Pb(II) adsorption on activated carbon obtained by pyrolysis of cow bone study. Journal of Analytical and Applied Pyrolysis, 89 (1), 122-128.

- Mao, J.A., Won, S.W., Vijayaraghavan, K. and Yun, Y.S. (2010), Immobilized citric acid-treated bacterial biosorbents for the removal of cationic pollutants. Chemical Engineering Journal, 162 (2), 662-668.

- Wu, Y.H., He, J.Z. and Yang, L.Z. (2010), Evaluating Adsorption and Biodegradation Mechanisms during the Removal of Microcystin-RR by Periphyton. Environmental Science & Technology, 44 (16), 6319-6324.

- Li, X.M., Zheng, W., Wang, D.B., Yang, Q., Cao, J.B., Yue, X., Shen, T.T. and Zeng, G.M. (2010), Removal of Pb (II) from aqueous solutions by adsorption onto modified areca waste: Kinetic and thermodynamic studies. Desalination, 258 (1-3), 148-153.

- Mohammad, M., Maitra, S., Ahmad, N., Bustam, A., Sen, T.K. and Dutta, B.K. (2010), Metal ion removal from aqueous solution using physic seed hull. Journal of Hazardous Materials, 179 (1-3), 363-372.

- Farooq, U., Kozinski, J.A., Khan, M.A. and Athar, M. (2010), Biosorption of heavy metal ions using wheat based biosorbents - A review of the recent literature. Bioresource Technology, 101 (14), 5043-5053.

- Miranda, M.A., Dhandapani, P., Kalavathy, M.H. and Miranda, L.R. (2010), Chemically activated Ipomoea carnea as an adsorbent for the copper sorption from synthetic solutions. Adsorption-Journal of the International Adsorption Society, 16 (1-2), 75-84.

- Ofomaja, A.E., Unuabonah, E.I. and Oladoja, N.A. (2010), Competitive modeling for the biosorptive removal of copper and lead ions from aqueous solution by Mansonia wood sawdust. Bioresource Technology, 101 (11), 3844-3852.

- Huang, L.Z., Zeng, G.M., Huang, D.L., Li, L.F., Du, C.Y. and Zhang, L. (2010), Biosorption of cadmium(II) from aqueous solution onto Hydrilla verticillata. Environmental Earth Sciences,  60 (8), 1683-1691.

- Chen, H., Dai, G.L., Zhao, J., Zhong, A.G., Wu, J.Y. and Yan, H. (2010), Removal of copper(II) ions by a biosorbent-Cinnamomum camphora leaves powder. Journal of Hazardous Materials, 177 (1-3), 228-236.

- Na, P., Jia, X.M., Bin, Y., Li, Y., Na, J., Chen, Y.C. and Wang, L.S. (2010), Arsenic adsorption on Ti-pillared montmorillonite. Journal of Chemical Technology and Biotechnology, 85 (5), 708-714.

- Zheng, L.C., Dang, Z., Yi, X.Y. and Zhang, H. (2010), Equilibrium and kinetic studies of adsorption of Cd(II) from aqueous solution using modified corn stalk. Journal of Hazardous Materials, 176 (1-3), 650-656.

- Qu, R.J., Zhang, Y., Sun, C.M., Wang, C.H., Ji, C.N., Chen, H. and Yin, P. (2010), Adsorption of Hg(II) from an Aqueous Solution by Silica-Gel Supported Diethylenetriamine Prepared via Different Routes: Kinetics, Thermodynamics, and Isotherms. Journal of Chemical and Engineering Data, 55 (4), 1496-1504.

- Zahra, N. (2010), Arsenic Contamination in Water and its Removal by using Different Low Cost Adsorbents. Journal of the Chemical Society of Pakistan, 32 (2), 259-264.

- Cretescu, I., Diaconu, M., Dughila, A., Stefanache, A. and Pohontu, C. (2010), Studies on the Biosorption of Terasil Dye by Aspergillus Niger Dead Biomass. Environmental Engineering and Management Journal, 9 (3), 335-339.

- Ngah, W.S.W. and Fatinathan, S. (2010), Adsorption characterization of Pb(II) and Cu(II) ions onto chitosan-tripolyphosphate beads: Kinetic, equilibrium and thermodynamic studies. Journal of Environmental Management, 91 (4), 958-969.

- Farooq, U., Khan, M.A., Athar, M., Sakina, M. and Ahmad, M. (2010), Environmentally Benign Urea-modifed Triticum aestivum Biomass for Lead (II) Elimination from Aqueous Solutions. Clean-Soil Air Water, 38 (1), 49-56.

- He, J., Hong, S., Zhang, L.A., Gan, F.X. and Ho, Y.S. (2010), Equilibrium and Thermodynamic Parameters of Adsorption of Methylene Blue Onto Rectorite. Fresenius Environmental Bulletin, 19 (11A), 2651-2656.

- Moradi, O., Zare, K., Monajjemi, M., Yari, M. and Aghaie, H. (2010), The Studies of Equilibrium and Thermodynamic Adsorption of Pb(II), Cd(II) and Cu(II) Ions from Aqueous Solution onto SWCNTs and SWCNT-COOH Surfaces. Fullerenes Nanotubes and Carbon Nanostructures, 18 (3), 285-302.

- Ngah, W.S.W. and Fatinathan, S. (2010), Pb(II) biosorption using chitosan and chitosan derivatives beads: Equilibrium, ion exchange and mechanism studies. Journal of Environmental Sciences-China, 22 (3), 338-346.

- Vazquez, G., Calvo, M., Freire, M.S., Gonzalez-Alvarez, J. and Antorrena, G. (2009), Chestnut shell as heavy metal adsorbent: Optimization study of lead, copper and zinc cations removal. Journal of Hazardous Materials, 172 (2-3), 1402-1414.

- Oladoja, N.A., Ololade, I.A., Idiaghe, J.A. and Egbon, E.E. (2009), Equilibrium isotherm analysis of the sorption of congo red by palm kernel coat. Central European Journal of Chemistry, 7 (4), 760-768.

- Pinzon-Bedoya, M.L. and Villamizar, L.E.V. (2009), Kinetc Modeling Biosorption of Cr(Iii) Using Orange Shell. Dyna-Colombia, 76 (160), 95-106.

- Karapinar, N. and Donat, R. (2009), Adsorption behaviour of Cu2+ and Cd2+ onto natural bentonite. Desalination, 249 (1), 123-129.

- Pavel, V.L., Bulgariu, D., Bulgariu, L., Hlihor, R.M. and Gavrilescu, M. (2009), Studies on Sorption and Transport Processes of Cadmium in Soils. Environmental Engineering and Management Journal, 8 (6), 1315-1320.

- El-Bayaa, A.A., Badawy, N.A. and AlKhalik, E.A. (2009), Effect of ionic strength on the adsorption of copper and chromium ions by vermiculite pure clay mineral. Journal of Hazardous Materials, 170 (2-3), 1204-1209.

- Huang, L.Z., Zeng, G.M., Huang, D.L., Li, L.F., Huang, P.M. and Xia, C.B. (2009), Adsorption of lead(II) from aqueous solution onto Hydrilla verticillata. Biodegradation, 20  (5), 651-660.

- Tang, Q., Tang, X.W., Li, Z.Z., Chen, Y.M., Kou, N.Y. and Sun, Z.F. (2009), Adsorption and desorption behaviour of Pb(II) on a natural kaolin: equilibrium, kinetic and thermodynamic studies. Journal of Chemical Technology and Biotechnology, 84 (9), 1371-1380.

- Zheng, H., Liu, D.H., Zheng, Y., Liang, S.P. and Liu, Z. (2009), Sorption isotherm and kinetic modeling of aniline on Cr-bentonite. Journal of Hazardous Materials, 167 (1-3), 141-147.

- Hong, S., Wen, C., He, J., Gan, F.X. and Ho, Y.S. (2009), Adsorption thermodynamics of Methylene Blue onto bentonite. Journal of Hazardous Materials, 167 (1-3), 630-633.

- az-Nava, C., Olguin, M.T., Solache-Rios, M., arcon-Herrera, M.T. and guilar-Elguezabal, A. (2009), Phenol sorption on surfactant-modified Mexican zeolitic-rich tuff in batch and continuous systems. Journal of Hazardous Materials, 167 (1-3), 1063-1069.

- Baker, H. (2009), Characterization for the interaction of nickel(II) and copper(II) from aqueous solutions with natural silicate minerals. Desalination, 244 (1-3), 48-58.

- Ozcan, A.S., Tunali, S., Akar, T. and Ozcan, A. (2009), Biosorption of lead(II) ions onto waste biomass of Phaseolus vulgaris L.: estimation of the equilibrium, kinetic and thermodynamic parameters. Desalination, 244 (1-3), 188-198.

- Aluyor, E.O., Oboh, I.O. and Obahiagbon, K.O. (2009), Equilibrium sorption isotherm for lead (Pb) ions on hydrogen peroxide modified rice hulls. International Journal of Physical Sciences, 4 (8), 423-427.

- Rauf, M.A., Qadri, S.M., Ashraf, S. and Al-Mansoori, K.M. (2009), Adsorption studies of Toluidine Blue from aqueous solutions onto gypsum. Chemical Engineering Journal, 150 (1), 90-95.

- Achak, M., Hafidi, A., Ouazzani, N., Sayadi, S. and Mandi, L. (2009), Low cost biosorbent "banana peel" for the removal of phenolic compounds from olive mill wastewater: Kinetic and equilibrium studies. Journal of Hazardous Materials, 166 (1), 117-125.

- Oo, C.W., Kassim, M.J. and Pizzi, A. (2009), Characterization and performance of Rhizophora apiculata mangrove polyflavonoid tannins in the adsorption of copper (II) and lead (II). Industrial Crops and Products, 30 (1), 152-161.

- Chabani, M., Amrane, A. and Bensmaili, A. (2009), Equilibrium sorption isotherms for nitrate on resin Amberlite IRA 400. Journal of Hazardous Materials, 165 (1-3), 27-33.

- Zhang, J., Xie, S.D. and Ho, Y.S. (2009), Removal of fluoride ions from aqueous solution using modified attapulgite as adsorbent. Journal of Hazardous Materials, 165 (1-3), 218-222.

- Amini, M., Younesi, H. and Bahramifar, N. (2009), Biosorption of nickel(II) from aqueous solution by Aspergillus niger: Response surface methodology and isotherm study. Chemosphere, 75 (11), 1483-1491.

- Bora, M.M., Dutta, N.N. and Rao, P.G. (2009), Extraction of Roselle dye from Roselle (Hibiscus sabdariffa) fruits by adsorption onto activated carbon: Equilibrium and kinetic studies. Journal of Scientific & Industrial Research, 68 (6), 555-559.

- Loutseti, S., Danielidis, D.B., Economou-Amilli, A., Katsaros, C., Santas, R. and Santas, P. (2009), The application of a micro-algal/bacterial biofilter for the detoxification of copper and cadmium metal wastes. Bioresource Technology, 100 (7), 2099-2105.

- Ofomaja, A.E. (2009), Equilibrium sorption of methylene blue using mansonia wood sawdust as biosorbent. Desalination and Water Treatment, 3 (1-3), 1-10.

- Hlihor, R.M. and Gavrilescu, M. (2009), Removal of Some Environmentally Relevant Heavy Metals Using Low-Cost Natural Sorbents. Environmental Engineering and Management Journal, 8 (2), 353-372.

- Tondi, G., Oo, C.W., Pizzi, A., Trosa, A. and Thevenon, M.F. (2009), Metal adsorption of tannin based rigid foams. Industrial Crops and Products, 29 (2-3), 336-340.

- Ozer, A., Gurbuz, G., Calimli, A. and Korbahti, B.K. (2009), Biosorption of copper(II) ions on Enteromorpha prolifera: Application of response surface methodology (RSM). Chemical Engineering Journal, 146 (3), 377-387.

- Barriada, J.L., Caridad, S., Lodeiro, P., Herrero, R. and de Vicente, M.E.S. (2009), Physicochemical characterisation of the ubiquitous bracken fern as useful biomaterial for preconcentration of heavy metals. Bioresource Technology, 100 (4), 1561-1567.

- Garcia-Mendieta, A., Solache-Rios, M. and Olguin, M.T. (2009), Evaluation of the sorption properties of a Mexican clinoptilolite-rich tuff for iron, manganese and iron-manganese systems. Microporous and Mesoporous Materials, 118 (1-3), 489-495.

- Ramakrishnan, M. and Nagarajan, S. (2009), Utilisation of Flame Tree Waste Biomass for the Removal of Hg(II) from Water. Acta Chimica Slovenica, 56 (1), 282-287.

- Turhan, K., Turak, F. and Ozgur, M.U. (2009), Sorption of Zn(II) and Pb(II) Ions by a New Resin Synthesized from Sumac Tannin and Gelatin. Innovations in Chemical Biology, ), 253-260.

- Turak, F., Turhan, K. and Ozgur, M.U. (2009), Sorption of Pb(II) and Zn(II) Ions from Aqueous Solution by Tannin Resins. Innovations in Chemical Biology, ), 277-283.

- Zheng, H., Han, L., Ma, H., Zheng, Y., Zhang, H., Liu, D. and Liang, S. (2008), Adsorption characteristics of ammonium ion by zeolite 13X. Journal of Hazardous Materials, 158 (2-3), 577-584.

- Salehi, P., Asghari, B. and Mohammadi, F. (2008), Removal of heavy metals from aqueous solutions by cercis siliquastrum L. Journal of the Iranian Chemical Society, 5), S80-S86.

- Ngah, W.S.W. and Fatinathan, S. (2008), Adsorption of Cu(II) ions in aqueous solution using chitosan beads, chitosan-GLA beads and chitosan-alginate beads. Chemical Engineering Journal,  143 (1-3), 62-72.

- Zheng, H., Wang, Y., Zheng, Y., Zhang, H.M., Liang, S.P. and Long, M. (2008), Equilibrium, kinetic and thermodynamic studies on the sorption of 4-hydroxyphenol on Cr-bentonite. Chemical Engineering Journal, 143 (1-3), 117-123.

- Ofomaja, A.E. and Ho, Y.S. (2008), Effect of temperatures and pH on methyl violet biosorption by Mansonia wood sawdust. Bioresource Technology, 99 (13), 5411-5417.

- Sud, D., Mahajan, G. and Kaur, M.P. (2008), Agricultural waste material as potential adsorbent for sequestering heavy metal ions from aqueous solutions - A review. Bioresource Technology, 99 (14), 6017-6027.

- Anirudhan, T.S. and Ramachandran, M. (2008), Synthesis and characterization of amidoximated polyacrylonitrile/organobentonite composite for Cu(II), Zn(II), and Cd(II) adsorption from aqueous solutions and industry wastewaters. Industrial & Engineering Chemistry Research, 47 (16), 6175-6184.

- Nadeem, R., Ansari, T.M. and Khalid, A.M. (2008), Fourier Transform Infrared Spectroscopic characterization and optimization of Pb(II) biosorption by fish (Labeo rohita) scales. Journal of Hazardous Materials, 156 (1-3), 64-73.

- Wang, X. and Min, B.G. (2008), Comparison of porous poly (vinyl alcohol)/hydroxyapatite composite cryogels and cryogels immobilized on poly (vinyl alcohol) and polyurethane foams for removal of cadmium. Journal of Hazardous Materials, 156 (1-3), 381-386.

- Ho, Y.S. and Wang, C.C. (2008), Sorption equilibrium of mercury onto ground-up tree fern. Journal of Hazardous Materials, 156 (1-3), 398-404.

- Bhattacharyya, K.G. and Sen Gupta, S. (2008), Adsorption of a few heavy metals on natural and modified kaolinite and montmorillonite: A review. Advances in Colloid and Interface Science, 140 (2), 114-131.

- Ozsoy, H.D., Kumbur, H., Saha, B. and van Leeuwen, J.H. (2008), Use of Rhizopus oligosporus produced from food processing wastewater as a biosorbent for Cu(II) ions removal from the aqueous solutions. Bioresource Technology, 99 (11), 4943-4948.

- Abia, A.A. and Asuquo, E.D. (2008), Sorption of Pb(II) and Cd(II) ions onto chemically unmodified and modified oil palm, fruit fibre adsorbent: Analysis of pseudo second order kinetic models. Indian Journal of Chemical Technology, 15 (4), 341-348.

- Guzel, F., Yakut, H. and Topal, G. (2008), Determination of kinetic and equilibrium parameters of the batch adsorption of Mn(II), Co(II), Ni(II) and Cu(II) from aqueous solution by black carrot (Daucus carota L.) residues. Journal of Hazardous Materials, 153 (3), 1275-1287.

- Arami, M., Limaee, N.Y. and Mahmoodi, N.M. (2008), Evaluation of the adsorption kinetics and equilibrium for the potential removal of acid dyes using a biosorbent. Chemical Engineering Journal, 139 (1), 2-10.

- Ngah, W.S.W. and Hanafiah, M.A.K.M. (2008), Adsorption of copper on rubber (Hevea brasiliensis) leaf powder: Kinetic, equilibrium and thermodynamic studies. Biochemical Engineering Journal, 39 (3), 521-530.

- Sener, S. (2008), Use of solid wastes of the soda ash plant as an adsorbent for the removal of anionic dyes: Equilibrium and kinetic studies. Chemical Engineering Journal, 138 (1-3), 207-214.

- Demirbas, O., Karadag, A., Alkan, M. and Dogan, M. (2008), Removal of copper ions from aqueous solutions by hazelnut shell. Journal of Hazardous Materials, 153 (1-2), 677-684.

- Bhattacharyya, K.G. and Sen Gupta, S. (2008), Influence of acid activation on adsorption of Ni(II) and Cu(II) on kaolinite and montmorillonite: Kinetic and thermodynamic study. Chemical Engineering Journal, 136 (1), 1-13.

- El Qada, E.N., Allen, S.J. and Walker, G.A. (2008), Adsorption of basic dyes from aqueous solution onto activated carbons. Chemical Engineering Journal, 135 (3), 174-184.

- Jain, N., Joshi, H.C., Dutta, S.C., Kumar, S. and Pathak, H. (2008), Biosorption of copper from wastewater using jatropha seed coat. Journal of Scientific & Industrial Research, 67 (2), 154-160.

- Monji, A.B., Ahmadi, S.J. and Zolfonoun, E. (2008), Selective biosorption of zirconium and hafnium from acidic aqueous solutions by rice bran, wheat bran and platanus orientalis tree leaves. Separation Science and Technology, 43 (3), 597-608.

- Koumanova, B., Achova, B. and Allen, S.J. (2008), Biosorption of acid dye on Pueraria lobata ohwi. Equilibrium and kinetic modelling.  International Journal of Environment and Pollution,  34 (1-4), 151-163.

- Wang, X.S. and Qin, Y. (2008), Removal of Ni2+ from aqueous solution by rice bran. International Journal of Environment and Pollution, 34 (1-4), 364-373.

- Wang, X. and Min, B.G. (2008), Cadmium sorption properties of poly(vinyl alcohol)/hydroxyapatite cryogels: II. Effects of operating parameters. Journal of Sol-Gel Science and Technology, 45 (1), 17-22.

- Mouta, E.R., Soares, M.R. and Casagrande, J.C. (2008), Copper adsorption as a function of solution parameters of variable charge soils. Journal of the Brazilian Chemical Society, 19 (5), 996-1009.

- Casagrande, J.C., Soaresl, M.R. and Moutal, E.R. (2008), Zinc adsorption in highly weathered soils. Pesquisa Agropecuaria Brasileira, 43 (1), 131-139.

- Calero, M., Hernainz, F., Blazquez, G., Martin-Lara, M.A. and Tenorio, G. (2008), Equilibrium modelling of Cr (VI) biosorption by olive stone. Waste Management and the Environment Iv, 109), 827-836.

- Sari, A., Tuzen, M., Citak, D. and Soylak, M. (2007), Equilibrium, kinetic and thermodynamic studies of adsorption of Pb(II) from aqueous solution onto Turkish kaolinite clay. Journal of Hazardous Materials, 149 (2), 283-291.

- Rudzinski, W. and Plazinski, W. (2007), Studies of the kinetics of solute adsorption at solid/solution interfaces: On the possibility of distinguishing between the diffusional and the surface reaction kinetic models by studying the pseudo-first-order kinetics. Journal of Physical Chemistry C, 111 (41), 15100-15110.

- Someda, H.H. (2007), Influence of the support base on the sorption of Co(II) with mixed solvents. Journal of Hazardous Materials, 149 (1), 189-198.

- Chai, L.Y., Wei, S.W., Peng, B. and Li, Z.Y. (2007), Adsorption of Ag(I) on H2TiO3 from aqueous solutions. Transactions of Nonferrous Metals Society of China, 17 (4), 832-835.

- Wu, C.H. (2007), Studies of the equilibrium and thermodynamics of the adsorption of Cu2+ onto as-produced and modified carbon nanotubes. Journal of Colloid and Interface Science, 311 (2), 338-346.

- Wang, X. and Min, B.G. (2007), Cadmium sorption properties of poly(vinyl alcohol)/hydroxyapatite cryogels: I. kinetic and isotherm studies. Journal of Sol-Gel Science and Technology, 43 (1), 99-104.

- Anirudhan, T.S., Unnithan, M.R., Divya, L. and Senan, P. (2007), Synthesis and characterization of polyacrylamide-grafted coconut coir pith having carboxylate functional group and adsorption ability for heavy metal ions. Journal of Applied Polymer Science, 104 (6), 3670-3681.

- Vilar, V.J.P., Botelho, C.M.S. and Boaventura, R.A.R. (2007), Kinetics and equilibrium modelling of lead uptake by algae Gelidium and algal waste from agar extraction industry. Journal of Hazardous Materials, 143 (1-2), 396-408.

- Igwe, J.C. and Abia, A.A. (2007), Adsorption kinetics and intraparticulate diffusivities for bioremediation of Co (II), Fe (II) and Cu (II) ions from waste water using modified and unmodified maize cob. International Journal of Physical Sciences, 2 (5), 119-127.

- Meenakshi, S. and Viswanathan, N. (2007), Identification of selective ion-exchange resin for fluoride sorption. Journal of Colloid and Interface Science, 308 (2), 438-450.

- Kundu, S. and Gupta, A.K. (2007), Adsorption characteristics of As(III) from aqueous solution on iron oxide coated cement (IOCC). Journal of Hazardous Materials, 142 (1-2), 97-104.

- Keskinkan, O., Goksu, M.Z.L., Yuceer, A. and Basibuyuk, M. (2007), Comparison of the adsorption capabilities of Myriophyllum spicatum and Ceratophyllum demersum for zinc, copper and lead. Engineering in Life Sciences, 7 (2), 192-196.

- Ozer, A. (2007), Removal of Pb(II) ions from aqueous solutions by sulphuric acid-treated wheat bran. Journal of Hazardous Materials, 141 (3), 753-761.

- Vijayaraghavan, K. and Yun, Y.S. (2007), Utilization of fermentation waste (Corynebacterium glutamicum) for biosorption of Reactive Black 5 from aqueous solution. Journal of Hazardous Materials, 141 (1), 45-52.

- Saltali, K., Sari, A. and Aydin, M. (2007), Removal of ammonium ion from aqueous solution by natural Turkish (Yildizeli) zeolite for environmental quality. Journal of Hazardous Materials, 141 (1), 258-263.

- Ngayila, N., Basly, J.P., Lejeune, A.H., Botineau, M. and Baudu, M. (2007), Myriophyllum alterniflorum DC., biomonitor of metal pollution and water quality. Sorption/accumulation capacities and photosynthetic pigments composition changes after copper and cadmium exposure. Science of the Total Environment, 373 (2-3), 564-571.

- Contreras, E.G., Martinez, B.E., Sepulveda, L.A. and Palma, C.L. (2007), Kinetics of basic dye adsorption onto sphagnum magellanicum peat. Adsorption Science & Technology, 25 (9), 637-646.

- Baker, H. and bdel-Halim, H.M. (2007), Removal of nickel ions from aqueous solutions by using insolubilized humic acid: Effect of pH and temperature. Asian Journal of Chemistry, 19 (1), 233-245.

- Ofomaja, A.E. and Ho, Y.S. (2007), Equilibrium sorption of anionic dye from aqueous solution by palm kernel fibre as sorbent. Dyes and Pigments, 74 (1), 60-66.

- Wang, X.S., Hu, H.Q. and Sun, C. (2007), Removal of copper (II) ions from aqueous solutions using Na-mordenite. Separation Science and Technology, 42 (6), 1215-1230.

- Jang, A., Lee, S.W., Seo, Y., Kim, K.W., Kim, I.S. and Bishop, P.L. (2007), Application of mulch for treating metals in urban runoff: batch and column test. Water Science and Technology, 55 (1-2), 95-103.

- Arami, M., Limaee, N.Y. and Mahmoodi, N.M. (2006), Investigation on the adsorption capability of egg shell membrane towards model textile dyes. Chemosphere, 65 (11), 1999-2008.

- de Castro, F.H.B., Garcia, G.B., de Hoces, M.C., Lara, M.A.M. and Jimenez, A.M. (2006), Use of solid of olive tree remainders in the biosorption of chromium. Afinidad, 63 (526), 454-460.

- El Qada, E.N., Allen, S.J. and Walker, G.M. (2006), Adsorption of Methylene Blue onto activated carbon produced from steam activated bituminous coal: A study of equilibrium adsorption isotherm. Chemical Engineering Journal, 124 (1-3), 103-110.

- Zaggout, F.R., Al-Subu, M.M. and El-Ghoti, T. (2006), Removal of cadmium (II) ions from aqueous solution by Tamrix gallica leaves. Journal of Environmental Engineering and Science, 5 (6), 509-515.

- Wankasi, D., Horsfall, M. and Spiff, A.I. (2006), Sorption kinetics of Pb2+ and Cu2+ ions from aqueous solution by Nipah palm (Nypa fruticans Wurmb) shoot biomass. Electronic Journal of Biotechnology, 9 (5), 587-592.

- de Hoces, M.C., de Castro, F.H.B., Garcia, G.B. and Rivas, G.T. (2006), Equilibrium modeling of removal of cadmium ions by olive stones. Environmental Progress, 25 (3), 261-266.

- Acar, F.N. and Eren, Z. (2006), Removal of Cu(II) ions by activated poplar sawdust (Samsun Clone) from aqueous solutions. Journal of Hazardous Materials, 137 (2), 909-914.

- Chao, A.C., Yu, S.H. and Chuang, G.S. (2006), Using NaCl particles as porogen to prepare a highly adsorbent chitosan membranes. Journal of Membrane Science, 280 (1-2), 163-174.

- King, P., Srinivas, P., Kumar, Y.P. and Prasad, V.S.R.K. (2006), Sorption of copper(II) ion from aqueous solution by Tectona grandis l.f. (teak leaves powder). Journal of Hazardous Materials, 136 (3), 560-566.

- Ho, Y.S. (2006), Review of second-order models for adsorption systems. Journal of Hazardous Materials, 136 (3), 681-689.

- Ozsoy, H.D. and Kumbur, H. (2006), Adsorption of Cu(II) ions on cotton boll. Journal of Hazardous Materials, 136 (3), 911-916.

- Hsieh, C.H., Lo, S.L., Kuan, W.H. and Chen, C.L. (2006), Adsorption of copper ions onto microwave stabilized heavy metal sludge. Journal of Hazardous Materials, 136 (2), 338-344.

- Mohan, D., Singh, K.P. and Singh, V.K. (2006), Trivalent chromium removal from wastewater using low cost activated carbon derived from agricultural waste material and activated carbon fabric cloth. Journal of Hazardous Materials, 135 (1-3), 280-295.

- Ozer, A., Akkaya, G. and Turabik, M. (2006), Biosorption of Acid Blue 290 (AB 290) and Acid Blue 324 (AB 324) dyes on Spirogyra rhizopus. Journal of Hazardous Materials, 135 (1-3), 355-364.

- Bhattacharyya, K.G. and Sen Gupta, S. (2006), Kaolinite, montmorillonite, and their modified derivatives as adsorbents for removal of Cu(II) from aqueous solution. Separation and Purification Technology, 50 (3), 388-397.

- Ngah, W.S.W., Kamari, A., Fatinathan, S. and Ng, P.W. (2006), Adsorption of chromium from aqueous solution using chitosan beads. Adsorption-Journal of the International Adsorption Society, 12 (4), 249-257.

- Montes-Hernandez, G. and Rihs, S. (2006), A simplified method to estimate kinetic and thermodynamic parameters on the solid-liquid separation of pollutants. Journal of Colloid and Interface Science, 299 (1), 49-55.

- Ho, Y.S. and Ofomaja, A.E. (2006), Biosorption thermodynamics of cadmium on coconut copra meal as biosorbent. Biochemical Engineering Journal, 30 (2), 117-123.

- Han, R.P., Zhang, J.H., Zou, W.H., Xiao, H.J., Shi, H. and Liu, H.M. (2006), Biosorption of copper(II) and lead(II) from aqueous solution by chaff in a fixed-bed column. Journal of Hazardous Materials, 133 (1-3), 262-268.

- Bhattacharyya, K.G. and Sen Gupta, S. (2006), Adsorption of Fe(III) from water by natural and acid activated clays: Studies on equilibrium isotherm, kinetics and thermodynamics of interactions. Adsorption-Journal of the International Adsorption Society, 12 (3), 185-204.

- Bhattacharyya, K.G. and Sen Gupta, S. (2006), Pb(II) uptake by kaolinite and montmorillonite in aqueous medium: Influence of acid activation of the clays. Colloids and Surfaces A-Physicochemical and Engineering Aspects, 277 (1-3), 191-200.

- Nityanandi, D. and Subbhuraam, C.V. (2006), Adsorptive removal of Pb(II) ions from aqueous solution using a coir-based product (Puresorbe). Adsorption Science & Technology, 24 (2), 177-191.

- Wang, X.S., Wang, J. and Sun, C. (2006), Removal of copper(II) ions from aqueous solutions using natural kaolinite. Adsorption Science & Technology, 24 (6), 517-530.

- Saltati, K. and Sari, A. (2006), Sorption capacity and thermodynamic properties of natural Turkish (Resadiye) bentonite for the removal of ammonium ions from aqueous solution. Adsorption Science & Technology, 24 (9), 749-760.

- Basso, M.C. and Cukierman, A.L. (2006), Wastewater treatment by chemically activated carbons from giant reed: Effect of the activation atmosphere on properties and adsorptive behavior. Separation Science and Technology, 41 (1), 149-165.

- Wang, X.S., Qin, Y. and Li, Z.F. (2006), Biosorption of zinc from aqueous solutions by rice bran: Kinetics and equilibrium studies. Separation Science and Technology, 41 (4), 747-756.

- Ho, Y.S. (2006), Second-order kinetic model for the sorption of cadmium onto tree fern: A comparison of linear and non-linear methods. Water Research, 40 (1), 119-125.

- Ozer, A., Akkaya, G. and Turabik, M. (2005), Biosorption of Acid Red 274 (AR 274) on Enteromorpha prolifera in a batch system. Journal of Hazardous Materials, 126 (1-3), 119-127.

- Oliveira, E.A., Montanher, S.F., Andrade, A.D., Nobrega, J.A. and Rollemberg, M.C. (2005), Equilibrium studies for the sorption of chromium and nickel from aqueous solutions using raw rice bran. Process Biochemistry, 40 (11), 3485-3490.

- Akkaya, G. and Ozer, A. (2005), Biosorption of Acid Red 274 (AR 274) on Dicranella varia: Determination of equilibrium and kinetic model parameters. Process Biochemistry, 40  (11), 3559-3568.

- Soares, M.R., Alleoni, L.R.F. and Casagrande, J.C. (2005), Thermodynamic parameters for boron adsorption reaction on highly weathered tropical soils. Quimica Nova, 28 (6), 1014-1022.

- Han, R.P., Zhang, J.H., Zou, W.H., Shi, H. and Liu, H.M. (2005), Equilibrium biosorption isotherm for lead ion on chaff. Journal of Hazardous Materials, 125 (1-3), 266-271.

- Singh, K.K., Rastogi, R. and Hasan, S.H. (2005), Removal of Cr(VI) from wastewater using rice bran. Journal of Colloid and Interface Science, 290 (1), 61-68.

- Dursun, A.Y. and Kalayci, C.S. (2005), Equilibrium, kinetic and thermodynamic studies on the adsorption of phenol onto chitin. Journal of Hazardous Materials, 123 (1-3), 151-157.

- Choy, K.K.H. and Mckay, G. (2005), Sorption of cadmium, copper, and zinc ions onto bone char using Crank diffusion model. Chemosphere, 60 (8), 1141-1150.

- Choy, K.K.H. and Mckay, G. (2005), Sorption of metal ions from aqueous solution using bone char. Environment International, 31 (6), 845-854.

- Ho, Y.S. (2005), Effect of pH on lead removal from water using tree fern as the sorbent. Bioresource Technology, 96 (11), 1292-1296.

- Zaggout, F.R. (2005), Kinetic removal of lead from water by decaying Tamrix leaves. Journal of Environmental Engineering and Science, 4 (4), 299-305.

- Erses, A.S., Fazal, M.A., Onay, T.T. and Craig, W.H. (2005), Determination of solid waste sorption capacity for selected heavy metals in landfills. Journal of Hazardous Materials, 121 (1-3), 223-232.

- Wang, X.S. and Qin, Y. (2005), Equilibrium sorption isotherms for of Cu2+ on rice bran. Process Biochemistry, 40 (2), 677-680.

- Montanher, S.F., Oliveira, E.A. and Rollemberg, M.C. (2005), Removal of metal ions from aqueous solutions by sorption onto rice bran.  Journal of Hazardous Materials, 117 (2-3), 207-211.

- Horsfall, M. and Spiff, A.I. (2005), Adsorption of transition metals in aqueous solutions by fluted pumpkin (Telfairia occidentalis HOOK f) waste. Chemistry & Biodiversity, 2 (9), 1266-1276.

- Jang, A., Seo, Y. and Bishop, P.L. (2005), The removal of heavy metals in urban runoff by sorption on mulch. Environmental Pollution, 133 (1), 117-127.

- Ho, Y.S., Chiang, T.H. and Hsueh, Y.M. (2005), Removal of basic dye from aqueous solution using tree fern as a biosorbent. Process Biochemistry, 40 (1), 119-124.

- Ozer, A., Ozer, D. and Ozer, A. (2004), The adsorption of copper(II) ions on to dehydrated wheat bran (DWB): determination of the equilibrium and thermodynamic parameters. Process Biochemistry, 39 (12), 2183-2191.

- Ho, Y.S. and Mckay, G. (2004), Sorption of copper(II) from aqueous solution by peat. Water Air and Soil Pollution, 158 (1), 77-97.

- Bhattacharyya, K.G. and Sharma, A. (2004), Adsorption of Pb(II) from aqueous solution by Azadirachta indica (Neem) leaf powder. Journal of Hazardous Materials, 113 (1-3), 97-109.

- Bektas, N., Agim, B.A. and Kara, S. (2004), Kinetic and equilibrium studies in removing lead ions from aqueous solutions by natural sepiolite. Journal of Hazardous Materials, 112 (1-2), 115-122.

- bu Al-Rub, F.A., El-Naas, M.H., Benyahia, F. and Ashour, I. (2004), Biosorption of nickel on blank alginate beads, free and immobilized algal cells. Process Biochemistry, 39  (11), 1767-1773.

- Horsfall, M., Spiff, A.I. and Abia, A.A. (2004), Studies on the influence of mercaptoacetic acid (MAA) modification of cassava (Manihot sculenta Cranz) waste biomass on the adsorption of Cu2+ and Cd2+ from aqueous solution. Bulletin of the Korean Chemical Society, 25 (7), 969-976.

- Baker, H. and Khalili, F. (2004), Analysis of the removal of lead(II) from aqueous solutions by adsorption onto insolubilized humic acid: temperature and pH dependence. Analytica Chimica Acta, 516 (1-2), 179-186.

- Ho, Y.S. (2004), Pseudo-isotherms using a second order kinetic expression constant. Adsorption-Journal of the International Adsorption Society, 10 (2), 151-158.

- Ho, Y.S. and Wang, C.C. (2004), Pseudo-isotherms for the sorption of cadmium ion onto tree fern. Process Biochemistry, 39 (6), 759-763.

- bu Al-Rub, F.A. (2004), Sorption of lead ions from simulated industrial wastewater onto Jordanian low-grade phosphate. Adsorption Science & Technology, 22 (2), 165-179.

- Keskinkan, O., Goksu, M.Z.L., Yuceer, A., Basibuyuk, M. and Forster, C.F. (2003), Heavy metal adsorption characteristics of a submerged aquatic plant (Myriophyllum spicatum). Process Biochemistry, 39 (2), 179-183.

- Ho, Y.S. (2003), Removal of metal ions from sodium arsenate solution using tree fern. Process Safety and Environmental Protection, 81 (B5), 352-356.