Last data updates: 19 June 2013

Ho, Y.S. and McKay, G. (2000), Batch sorber design using equilibrium and contact time data for the removal of lead. Water Air and Soil Pollution, 124 (1-2), 141-153.

| Document type: Article | Language: English | Cited References: 28 | Times Cited: 25 | Times self cited: 1 |
| --- | --- | --- | --- | --- |

Abstract: The two-stage batch sorption design of the sorption of lead ions onto peat has been studied based on a Langmuir isotherm type equation obtained from different contact time studies. A model has been developed to predict the optimised minimum operating time to determine a specified amount of lead removal. The sorption capacity at any contact time has been evaluated with an equation also based on the mathematical form of the Langmuir equation.

Keywords: Batch Sorption, Contact Time Optimisation, Langmuir Equation, Lead Ions, Two-Stage, Aqueous-Solutions, Fly-Ash, Hexavalent Chromium, Waste-Water, Adsorption, Peat, Sorption, Cadmium, Ions, Kinetics

Addresses:

McKay G, Hong Kong Univ Sci & Technol, Dept Chem Engn, Clear Water Bay, Kowloon, Hong Kong, Peoples R China

Hong Kong Univ Sci & Technol, Dept Chem Engn, Kowloon, Hong Kong, Peoples R China

- Ganguly, A., Guha, A.K. and Ray, L. (2011), Adsorption behaviour of cadmium by Bacillus cereus M-16(1): some physical and biochemical studies. Chemical Speciation and Bioavailability, 23 (3), 175-182.

- Anirudhan, T.S., Rijith, S. and Tharun, A.R. (2010), Adsorptive removal of thorium(IV) from aqueous solutions using poly(methacrylic acid)-grafted chitosan/bentonite composite matrix: Process design and equilibrium studies. Colloids and Surfaces A-Physicochemical and Engineering Aspects, 368 (1-3), 13-22.

- Oladoja, N.A., Ofomaja, A.E., Idiaghe, J.A., Akinlabi, A.K. and Egbon, E.E. (2010), Sorption of Cu (II) ion from aqueous solution by scrap tyre. Desalination and Water Treatment, 16 (1-3), 83-94.

- Unuabonah, E.I., Olu-Owolabi, B.I., Okoro, D. and Adebowale, K.O. (2009), Comparison of two-stage sorption design models for the removal of lead ions by polyvinyl-modified Kaolinite clay. Journal of Hazardous Materials, 171 (1-3), 215-221.

- Unuabonah, E.I. and Adebowale, K.O. (2009), Optimization of kinetic data for two-stage batch adsorption of Pb(II) ions onto tripolyphosphate-modified kaolinite clay. Journal of Chemical Technology and Biotechnology, 84 (11), 1726-1735.

- Unuabonah, E.I., Adebowale, K.O. and Ofomaja, A.E. (2009), Two-stage Batch Adsorber Design: A Time-Dependent Langmuir Model for Adsorption of Pb2+ and Cd2+ onto Modified Kaolinite Clay. Water Air and Soil Pollution, 200 (1-4), 133-145.

- Atolaiye, B.O., Babalola, J.O., Adebayo, M.A. and Aremu, M.O. (2009), Equilibrium modeling and pH-dependence of the adsorption capacity of Vitex doniana leaf for metal ions in aqueous solutions. African Journal of Biotechnology, 8 (3), 507-514.

- Oladoja, N.A., Aboluwoye, C.O., Oladimeji, Y.B., Ashogbon, A.O. and Otemuyiwa, I.O. (2008), Studies on castor seed shell as a sorbent in basic dye contaminated wastewater remediation. Desalination, 227 (1-3), 190-203.

- Vilar, V.J.P., Botelho, C.M.S. and Boaventura, R.A.R. (2007), Kinetics and equilibrium modelling of lead uptake by algae Gelidium and algal waste from agar extraction industry. Journal of Hazardous Materials, 143 (1-2), 396-408.

- Feo, J.C., Ordonez, E., Letek, M., Castro, M.A., Munoz, M.I., Gil, J.A., Mateos, L.M. and Aller, A.J. (2007), Retention of inorganic arsenic by coryneform mutant strains. Water Research, 41 (3), 531-542.

- Khazali, O., bu-El-Halawa, R. and Al-Sou'od, K. (2007), Removal of copper(II) from aqueous solution by Jordanian pottery materials. Journal of Hazardous Materials, 139 (1), 67-71.

- Arslan, G., Cetin, S. and Pehlivan, E. (2007), Removal of Cu(II) and Ni(II) from aqueous solution by lignite-based humic acids. Energy Sources Part A-Recovery Utilization and Environmental Effects, 29 (7), 619-630.

- Tsekova, K., Ianis, M. and Ganeva, S. (2007), Biosorption of binary mixtures of copper and cobalt by Penicillium cyclopium biomass. Comptes Rendus de l Academie Bulgare des Sciences, 60 (1), 63-70.

- Ozacar, M. and Sengil, I.A. (2006), A two stage batch adsorber design for methylene blue removal to minimize contact time. Journal of Environmental Management, 80 (4), 372-379.

- Ozacar, M. (2006), Contact time optimization of two-stage batch adsorber design using second-order kinetic model for the adsorption of phosphate onto alunite. Journal of Hazardous Materials, 137 (1), 218-225.

- Bhattacharyya, K.G. and Sen Gupta, S. (2006), Pb(II) uptake by kaolinite and montmorillonite in aqueous medium: Influence of acid activation of the clays. Colloids and Surfaces A-Physicochemical and Engineering Aspects, 277 (1-3), 191-200.

- Ozacar, M. (2005), Response to comment on "Two-stage batch sorber design using second-order kinetic model for the sorption of metal complex dyes onto pine sawdust" by Dr. Y.-S. Ho, Biochem. Eng. J. 21 (2004) 39-45. Biochemical Engineering Journal, 23 (3), 293.

- Kaynak, G., Ersoz, M. and Kara, H. (2004), Investigation of the properties of oil at the bleaching unit of an oil refinery. Journal of Colloid and Interface Science, 280 (1), 131-138.

- Ho, Y.S. and Mckay, G. (2004), Sorption of copper(II) from aqueous solution by peat. Water Air and Soil Pollution, 158 (1), 77-97.

- Bhattacharyya, K.G. and Sharma, A. (2004), Adsorption of Pb(II) from aqueous solution by Azadirachta indica (Neem) leaf powder. Journal of Hazardous Materials, 113 (1-3), 97-109.

- Ozacar, M. and Sengyl, I.A. (2004), Two-stage batch sorber design using second-order kinetic model for the sorption of metal complex dyes onto pine sawdust. Biochemical Engineering Journal, 21 (1), 39-45.

- Ozacar, M. and Sengil, I.A. (2004), Equilibrium data and process design for adsorption of disperse dyes onto alunite. Environmental Geology, 45 (6), 762-768.

- Annadurai, G., Juang, R.S., Yen, P.S. and Lee, D.J. (2003), Use of thermally treated waste biological sludge as dye absorbent. Advances in Environmental Research, 7 (3), 739-744.

- Vaughan, R.L., Reed, B.E., Jensen, J.E. and Matsumoto, M.R. (2001), Physicochemical Processes. Water Environment Research , 73 (5), 278-371.

- Pennell, K.D., Costanza, J., Kong, L.J., Martin, C.A., Ramsburg, C.A. and Taylor, T.P. (2001), Groundwater Quality. Water Environment Research, 73 (5), 1308-1467.

- Ray, L., Paul, S., Bera, D. and Chattopadhyay, P. (2005), Bioaccumulation of Pb(II) from aqueous solutions by Bacillus Cereus M116. Journal for Hazardous Substance Research, 5 (1), 1-21.