Last data updates: 07 November 2014

Ho, Y.S. and McKay, G. (2004), Sorption of copper(II) from aqueous solution by peat. Water Air and Soil Pollution, 158 (1), 77-97.

| Document type: Article | Language: English | Cited References: 68 | Times Cited: 45 | Times self cited: 3 |
| --- | --- | --- | --- | --- |

Abstract: The use of peat for removal of copper(II) from aqueous solution has been investigated at various initial copper ion concentrations and masses of peat. The equilibrium sorption study can be described by the Langmuir equation and defined in terms of the operating lines for each batch contacting system. The mechanisms of the rate of sorption of copper(II) were analysed using the Elovich equation and a pseudo-second-order model. Both rate mechanisms provided a very high degree of correlation of the experimental sorption rate data suggesting either model could be used in design applications.

Keywords: Copper, Kinetics, Peat, Sorption, Intraparticle Mass-Transport, Agricultural By-Products, Sphagnum Moss Peat, Heavy-Metals, Waste-Water, Humic-Acid, Efficient Removal, Elovich Equation, Activated Carbon, Organic-Matter

Addresses: McKay G, Hong Kong Univ Sci & Technol, Dept Chem Engn, Clear Water Bay, Kowloon, Hong Kong

Hong Kong Univ Sci & Technol, Dept Chem Engn, Kowloon, Hong Kong

- Arabyarmohammadi, H., Salarirad, M.M. and Behnamfard, A. (2014), Characterization and utilization of clay-based construction and demolition wastes as adsorbents for zinc(II) removal from aqueous solutions: an equilibrium and kinetic study. Environmental Progress & Sustainable Energy, 33 (3), 777-789.

- Ma, A., Hadi, P., Barford, J., Hui, C.W. and McKay, G. (2014), Modified Empty Bed Residence Time Model for Copper Removal. Industrial & Engineering Chemistry Research, 53 (35), 13773-13781.

- Brannvall, E., Zamora, C.B., Sjoblom, R. and Kumpiene, J. (2014), Effect of industrial residue combinations on availability of elements. Journal of Hazardous Materials, 276), 171-181.

- Nadeem, R., Zafar, M.N., Afzal, A., Hanif, M.A. and Saeed, R. (2014), Potential of NaOH pretreated Mangifera indica waste biomass for the mitigation of Ni(II) and Co(II) from aqueous solutions. Journal of the Taiwan Institute of Chemical Engineers, 45 (3), 967-972.

- Abidin, Z.Z., Mohd Salleh, M.A., Harun, M.Y. and bu Bakar, N. (2014), Biosorption of Zn (II) from aqueous solution by jatropha curcas press cake. Journal of Scientific & Industrial Research, 73 (3), 191-194.

- Ortiz-Oliveros, H.B., Flores-Espinosa, R.M., Ordonez-Regil, E. and Fernandez-Valverde, S.M. (2014), Synthesis of alpha-Ti(HPO4)(2)center dot H2O and sorption of Eu (III). Chemical Engineering Journal, 236), 398-405.

- Saleem, M. and Lee, K.H. (2014), Selective fluorescence detection of Cu2+ in aqueous solution and living cells. Journal of Luminescence, 145), 843-848.

- Meneghel, A.P., Goncalves, A.C., Tarley, C.R.T., Stangarlin, J.R., Rubio, F. and Nacke, H. (2014), Studies of Pb2+ adsorption by Moringa oleifera Lam. seeds from an aqueous medium in a batch system. Water Science and Technology, 69 (1), 163-169.

- Sadia, M., Jan, M.R., Shah, J. and Greenway, G.M. (2013), Simultaneous preconcentration and determination of nickel and cobalt using functionalised mesoporous silica spheres by ICP-OES. International Journal of Environmental Analytical Chemistry, 93 (14), 1537-1556.

- Milenkovic, D.D., Milosavljevic, M.M., Marinkovic, A.D., Dokic, V.R., Mitrovic, J.Z. and Bojic, A.L. (2013), Removal of copper(II) ion from aqueous solution by high-porosity activated carbon. Water Sa, 39 (4), 515-522.

- Malarvizhi, T.S. and Santhi, T. (2013), Lignite fired fly ash modified by chemical treatment for adsorption of zinc from aqueous solution. Research on Chemical Intermediates, 39 (6), 2473-2494.

- He, W., Zhang, Y.Y., Tian, R., Hu, H.X., Chen, B., Chen, L.K. and Xu, F.L. (2013), Modeling the purification effects of the constructed Sphagnum wetland on phosphorus and heavy metals in Dajiuhu Wetland Reserve, China. Ecological Modelling, 252), 23-31.

- Meneghel, A.P., Goncalves, A.C., Rubio, F., Dragunski, D.C., Lindino, C.A. and Strey, L. (2013), Biosorption of Cadmium from Water Using Moringa (Moringa oleifera Lam.) Seeds. Water Air and Soil Pollution, 224 (3.

- Robalds, A., Klavins, M. and Dreijalte, L. (2013), Sorption of thallium(I) ions by peat. Water Science and Technology, 68 (10), 2208-2213.

- Visa, M., Isac, L. and Duta, A. (2012), Fly ash adsorbents for multi-cation wastewater treatment. Applied Surface Science , 258 (17), 6345-6352.

- Albarelli, J.Q., Luna, M.T., Vieira, R.S. and Beppu, M.M. (2012), Evaluation of Glass Beads Coated with Chitosan for the Adsorption of Copper(II) Ions from Aqueous Solution. Adsorption Science & Technology, 30 (3), 227-240.

- Albadarin, A.B., Mangwandi, C., Al-Muhtaseb, A.H., Walker, G.M., Allen, S.J. and Ahmad, M.N.M. (2012), Kinetic and thermodynamics of chromium ions adsorption onto low-cost dolomite adsorbent. Chemical Engineering Journal, 179), 193-202.

- Benavente, M., Moreno, L. and Martinez, J. (2011), Sorption of heavy metals from gold mining wastewater using chitosan. Journal of the Taiwan Institute of Chemical Engineers, 42 (6), 976-988.

- Nikiforova, T.E. and Kozlov, V.A. (2011), Various factors affecting heavy metal ion sorption from aqueous media by sorbent containing cellulose. Protection of Metals and Physical Chemistry of Surfaces , 47 (1), 20-24.

- Sathishkumar, M., Pavagadhi, S., Vijayaraghavan, K., Balasubramanian, R. and Ong, S.L. (2010), Experimental studies on removal of microcystin-LR by peat. Journal of Hazardous Materials,  184 (1-3), 417-424.

- Ghaee, A., Shariaty-Niassar, M., Barzin, J. and Matsuura, T. (2010), Effects of chitosan membrane morphology on copper ion adsorption. Chemical Engineering Journal, 165 (1), 46-55.

- Nikiforova, T.E. and Kozlov, V.A. (2010), Specific features of sorption of heavy metal ions by a cellulose-containing sorbent from aqueous media. Russian Journal of Applied Chemistry, 83 (10), 1781-1784.

- Vazquez, G., Freire, M.D., Gonzalez-Alvarez, J. and Antorrena, G. (2009), Equilibrium and kinetic modelling of the adsorption of Cd2+ ions onto chestnut shell. Desalination, 249 (2), 855-860.

- Nityanandi, D. and Subbhuraam, C.V. (2009), Kinetics and thermodynamic of adsorption of chromium(VI) from aqueous solution using puresorbe. Journal of Hazardous Materials, 170 (2-3), 876-882.

- Caramalau, C., Bulgariu, L. and Macoveanu, M. (2009), Adsorption Characteristics of Co(Ii) Ions from Aqueous Solutions on Romanian Peat Moss. Environmental Engineering and Management Journal, 8 (5), 1089-1095.

- Hanafiah, M.A.K.M., Zakaria, H. and Ngah, W.S.W. (2009), Preparation, Characterization, and Adsorption Behavior of Cu(II) Ions onto Alkali-Treated Weed (Imperata cylindrica) Leaf Powder. Water Air and Soil Pollution, 201 (1-4), 43-53.

- Dikici, H. (2009), Adsorption of Divalent Metal Ions on a Herbaceous Peat. Asian Journal of Chemistry, 21 (5), 3334-3342.

- Wang, X., Zhao, C.M., Zhao, P., Dou, P.P., Ding, Y. and Xu, P. (2009), Gellan gel beads containing magnetic nanoparticles: An effective biosorbent for the removal of heavy metals from aqueous system. Bioresource Technology, 100 (7), 2301-2304.

- Cho, Y. and Komarneni, S. (2009), Effect of particle size on cesium exchange kinetics by K-depleted phlogopite. Applied Clay Science, 43 (3-4), 401-407.

- Bulgariu, L., Ratoi, M., Bulgariu, D. and Macoveanu, M. (2009), The Sorption of Lead(Ii) Ions from Aqueous Solutions on Peat: Kinetics Study. Environmental Engineering and Management Journal, 8 (2), 289-295.

- Hlihor, R.M. and Gavrilescu, M. (2009), Removal of Some Environmentally Relevant Heavy Metals Using Low-Cost Natural Sorbents. Environmental Engineering and Management Journal, 8 (2), 353-372.

- Badmus, M.A.O. and Audu, T.O.K. (2009), Periwinkle Shell: Based Granular Activated Carbon for Treatment of Chemical Oxygen Demand (Cod) in Industrial Wastewater. Canadian Journal of Chemical Engineering, 87 (1), 69-77.

- Zhang, D.F., Huang, S., Lv, J., Shi, C.B. and Xu, Z.H. (2009), Research on Nitrogen and Phosphorus Removal by Modified Zeolite Associated with Modified Peat from Micro-polluted Scenic-water. Iceet: 2009 International Conference on Energy and Environment Technology, Vol 2, Proceedings, ), 709-712.

- Ma, A., Shek, T.H., Allen, S.J., Lee, V.K.C. and Mckay, G. (2008), Removal of nickel from effluents by chelating ion exchange. Journal of Chemical Technology and Biotechnology, 83 (12), 1623-1632.

- Rivas, F.J., de la Calle, R.G., Alvarez, P. and Acedo, B. (2008), Polycyclic aromatic hydrocarbons sorption on soils: Some anomalous isotherms. Journal of Hazardous Materials, 158 (2-3), 375-383.

- Ulmanu, M., Anger, I., Fernandez, Y., Castrillon, L. and Maranon, E. (2008), Batch chromium(VI), cadmium(II) and lead(II) removal from aqueous solutions by horticultural peat. Water Air and Soil Pollution, 194 (1-4), 209-216.

- Kalmykova, Y., Stromvall, A.M. and Steenari, B.M. (2008), Adsorption of cd, cu, ni, pb and zn on Sphagnum peat from solutions with low metal concentrations. Journal of Hazardous Materials, 152 (2), 885-891.

- Jain, N., Joshi, H.C., Dutta, S.C., Kumar, S. and Pathak, H. (2008), Biosorption of copper from wastewater using jatropha seed coat. Journal of Scientific & Industrial Research, 67 (2), 154-160.

- Bulgariu, L., Cojocaru, C., Robu, B. and Macoveanu, M. (2007), Equilibrium isotherms studies for sorption of lead ions from aqueous solutions using Romanian peat sorbent. Environmental Engineering and Management Journal, 6 (5), 425-430.

- Fei, Q. and Bei, W. (2007), Single- and multi-component adsorption of Pb, Cu, and Cd on peat. Bulletin of Environmental Contamination and Toxicology, 78 (3-4), 265-269.

- Klucakova, M. and Pekar, M. (2006), New model for equilibrium sorption of metal ions on solid humic acids. Colloids and Surfaces A-Physicochemical and Engineering Aspects, 286 (1-3), 126-133.

- Ho, Y.S. (2006), Review of second-order models for adsorption systems. Journal of Hazardous Materials, 136 (3), 681-689.

- Kumar, K.V. and Sivanesan, S. (2006), Selection of optimum sorption kinetics: Comparison of linear and non-linear method. Journal of Hazardous Materials, 134 (1-3), 277-279.

- Kucukgul, E.Y. and Kudu, S. (2006), Zinc and copper adsorption from an aqueous solution onto activated carbon. Fresenius Environmental Bulletin, 15 (6), 512-517.

- Chefetz, B., Sominski, L., Pinchas, A., Ginsburg, T., Elmachliy, S., Tel-Or, E. and Gedanken, A. (2005), New approach for the removal of metal ions from water: Adsorption onto aquatic plants and microwave reaction for the fabrication of nanometals. Journal of Physical Chemistry B, 109 (32), 15179-15181.