Last data updates: 19 June 2013

Ho, Y.S., Wase, D.A.J. and Forster, C.F. (1996), Removal of lead ions from aqueous solution using sphagnum moss peat as adsorbent. Water SA, 22 (3), 219-224.

| Document type: Article | Language: English | Cited References: 28 | Times Cited: 41 | Times self cited: 6 |
| --- | --- | --- | --- | --- |

Abstract: The use of sphagnum moss peat for the removal of lead from aqueous solution has been studied in batch experiments. Investigations include the effect of pH and temperature and kinetics of adsorption. The adsorption equilibria data were found to follow Langmuir models. It was found that the efficiency of lead removal using sphagnum moss peat as adsorbent depended very little either on the reaction temperatures (10 to 40°C) or on the initial pH values (4.0 to 6.0). Kinetic data suggested that the adsorption process was endothermic and pore diffusion was not the only rate-determining step.

Keywords: Cross-Flow Microfiltration, Heavy-Metals, Adsorption, Effluents, Waste, Clay

Addresses: Univ Birmingham, Sch Civil Engn, Birmingham, W Midlands B15 2TT England

Univ Birmingham, Sch Chem Engn, Birmingham, W Midlands B15 2TT England

- Dongre, R., Thakur, M., Ghugal, D. and Meshram, J. (2012), Bromine pretreated chitosan for adsorption of lead (II) from water. Bulletin of Materials Science, 35 (5), 875-884.

- Fil, B.A., Boncukcuoglu, R., Yilmaz, A.E. and Bayar, S. (2012), Adsorption of Ni(II) on ion exchange resin: Kinetics, equilibrium and thermodynamic studies. Korean Journal of Chemical Engineering, 29 (9), 1232-1238.

- Fil, B.A., Boncukcuoglu, R., Yilmaz, A.E. and Bayar, S. (2012), Adsorption Kinetics and Isotherms for the Removal of Zinc Ions from Aqueous Solutions by an Ion-Exchange Resin. Journal of the Chemical Society of Pakistan, 34 (4), 841-848.

- Dikmen, S. and Yorukogullari, E. (2011), Nitrate Removal from Aqueous Solution by Hexadecyltrimethylammonium Bromide-Modified Clinoptilolite. Asian Journal of Chemistry, 23 (6), 2653-2660.

- Al-Haidary, A.M.A., Zanganah, F.H.H., Al-Azawi, S.R.F., Khalili, F.I. and Al-Dujaili, A.H. (2011), A Study on Using Date Palm Fibers and Leaf Base of Palm as Adsorbents for Pb(II) Ions from Its Aqueous Solution. Water Air and Soil Pollution, 214 (1-4), 73-82.

- Adie, D.B., Olarinoye, N.O., Oke, I.A., Ismail, A., Lukman, S. and Otun, J.A. (2010), Removal of Lead Ions from Aqueous Solutions Using Powdered Corn Cobs. Canadian Journal of Chemical Engineering, 88 (2), 241-255.

- Oladoja, N.A., Ofomaja, A.E., Idiaghe, J.A., Akinlabi, A.K. and Egbon, E.E. (2010), Sorption of Cu (II) ion from aqueous solution by scrap tyre. Desalination and Water Treatment, 16 (1-3), 83-94.

- Xiong, X.J., Meng, X.J. and Zheng, T.L. (2010), Biosorption of CI Direct Blue 199 from aqueous solution by nonviable Aspergillus niger.  Journal of Hazardous Materials, 175 (1-3), 241-246.

- Hu, M.H., Li, Y.Q., Sun, M. and Ao, Y.S. (2009), Effects of temperature on the release of nutrient elements of solid organic materials under conditions of oversaturation. Waste Management, 29 (12), 3029-3035.

- Jayaram, K. and Prasad, M.N.V. (2009), Removal of Pb(II) from aqueous solution by seed powder of Prosopis juliflora DC. Journal of Hazardous Materials, 169 (1-3), 991-997.

- Jayaram, K., Murthy, I.Y.L.N., Lalhruaitluanga, H. and Prasad, M.N.V. (2009), Biosorption of lead from aqueous solution by seed powder of Strychnos potatorum L. Colloids and Surfaces B-Biointerfaces, 71 (2), 248-254.

- Bulgariu, L., Ratoi, M., Bulgariu, D. and Macoveanu, M. (2009), Adsorption potential of mercury(II) from aqueous solutions onto Romanian peat moss. Journal of Environmental Science and Health Part A-Toxic/Hazardous Substances & Environmental Engineering, 44 (7), 700-706.

- Asandei, D., Bulgariu, L. and Bobu, E. (2009), Lead (Ii) Removal from Aqueous Solutions by Adsorption Onto Chitosan. Cellulose Chemistry and Technology, 43 (4-6), 211-216.

- Bulgariu, L., Ratoi, M., Bulgariu, D. and Macoveanu, M. (2009), The Sorption of Lead(Ii) Ions from Aqueous Solutions on Peat: Kinetics Study. Environmental Engineering and Management Journal, 8 (2), 289-295.

- Bulgariu, L., Bulgariu, D., Malutan, T. and Macoveanu, M. (2009), Adsorption of Lead(II) Ions from Aqueous Solution onto Lignin. Adsorption Science & Technology, 27 (4), 435-445.

- Bulgariu, L., Ratoi, M., Bulgariu, D. and Macoveanu, M. (2008), Equilibrium Study of Pb(Ii) and Hg(Ii) Sorption from Aqueous Solutions by Moss Peat. Environmental Engineering and Management Journal, 7 (5), 511-516.

- Gunay, A., Arslankaya, E. and Tosun, I. (2007), Lead removal from aqueous solution by natural and pretreated clinoptilolite: Adsorption equilibrium and kinetics. Journal of Hazardous Materials, 146 (1-2), 362-371.

- Erenturk, S. and Malkoc, E. (2007), Removal of lead(II) by adsorption onto Viscum album L.: Effect of temperature and equilibrium isotherm analyses. Applied Surface Science, 253 (10), 4727-4733.

- Issabayeva, G., Aroua, M.K. and Sulaiman, N.M.N. (2006), Removal of lead from aqueous solutions on palm shell activated carbon. Bioresource Technology, 97 (18), 2350-2355.

- Ho, Y.S. and Ofomaja, A.E. (2006), Pseudo-second-order model for lead ion sorption from aqueous solutions onto palm kernel fiber. Journal of Hazardous Materials, 129 (1-3), 137-142.

- Murathan, A.S. and Butun, M. (2006), Removal of lead ions from dilute aqueous solution in packed columns by using natural fruit shells through adsorption. Fresenius Environmental Bulletin, 15 (12A), 1491-1498.

- Mussatto, S.I., Dragone, G. and Roberto, I.C. (2006), Brewers' spent grain: generation, characteristics and potential applications. Journal of Cereal Science, 43 (1), 1-14.

- Saxena, A. (2006), Seasonal pattern of metal bioaccumulation and their toxicity on Sphagnum squarrosum. Journal of Environmental Biology, 27 (1), 71-75.

- Bulut, Y. and Baysal, Z. (2006), Removal of Pb(II) from wastewater using wheat bran. Journal of Environmental Management, 78 (2), 107-113.

- Wankasi, D., Horsfall, M. and Spiff, A.I. (2005), Retention of Pb (II) ion from aqueous solution by Nipah palm (Nypa fruticans Wurmb) petiole biomass. Journal of the Chilean Chemical Society, 50 (4), 691-696.

- Ho, Y.S. and Ofomaja, A.E. (2005), Kinetics and thermodynamics of lead ion sorption on palm kernel fibre from aqueous solution. Process Biochemistry, 40 (11), 3455-3461.

- Dursun, A.Y. and Kalayci, C.S. (2005), Equilibrium, kinetic and thermodynamic studies on the adsorption of phenol onto chitin. Journal of Hazardous Materials, 123 (1-3), 151-157.

- Horsfall, M. and Spiff, A.I. (2005), Equilibrium sorption study of Al3+, Co2+ and Ag+ in aqueous solutions by fluted pumpkin (Telfairia occidentalis HOOK f) waste biomass. Acta Chimica Slovenica, 52 (2), 174-181.

- Horsfall, M., Ogban, F. and Akporhonor, E.E. (2005), Biosorption of Pb2+ from aqueous solution by waste biomass of aerial roots of Rhizophora mangle (red mangrove). Chemistry & Biodiversity, 2 (9), 1246-1255.

- Horsfall, M. and Spiff, A.I. (2005), Adsorption of transition metals in aqueous solutions by fluted pumpkin (Telfairia occidentalis HOOK f) waste. Chemistry & Biodiversity, 2 (9), 1266-1276.

- Ofomaja, E.A., Unuabonah, I.E. and Oladoja, N.A. (2005), Removal of lead from aqueous solution by palm kernel fibre. South African Journal of Chemistry-Suid-Afrikaanse Tydskrif Vir Chemie, 58), 127-130.

- Ho, Y.S., Chiu, W.T., Hsu, C.S. and Huang, C.T. (2004), Sorption of lead ions from aqueous solution using tree fern as a sorbent. Hydrometallurgy, 73 (1-2), 55-61.

- Petroni, S.L.G., Pires, M.A.F. and Munita, C.S. (2004), Use of radiotracer in adsorption studies of copper on peat. Journal of Radioanalytical and Nuclear Chemistry, 259 (2), 239-243.

- Ng, J.C.Y., Cheung, W.H. and Mckay, G. (2003), Equilibrium studies for the sorption of lead from effluents using chitosan. Chemosphere, 52 (6), 1021-1030.

- Marin, J. and Ayele, J. (2003), Removal of some heavy metal cations from aqueous solutions by spruce sawdust. II. Adsorption-desorption through column experiments. Environmental Technology,  24 (4), 491-502.

- Godlewska-Zylkiewicz, B. (2001), Analytical applications of living organisms for preconcentration of trace metals and their speciation.  Critical Reviews in Analytical Chemistry, 31 (3), 175-189.

- Woolard, C.D., Petrus, K. and van der Horst, M. (2000), The use of a modified fly ash as an adsorbent for lead. Water Sa, 26 (4), 531-536.

- Ho, Y.S. and Mckay, G. (1999), Batch lead (II) removal from aqueous solution by peat: Equilibrium and kinetics. Process Safety and Environmental Protection, 77 (B3), 165-173.

- Quek, S.Y., Wase, D.A.J. and Forster, C.F. (1998), The use of sago waste for the sorption of lead and copper. Water Sa, 24 (3), 251-256.

- Quek, S.Y., Al-Duri, B., Wase, D.A.J. and Forster, C.F. (1998), Coir as a biosorbent of copper and lead. Process Safety and Environmental Protection, 76 (B1), 50-54.

- Mohammad, A. and Najar, M. (1997), Physico-chemical adsorption treatments for minimization of heavy metal contents in water and wastewaters. Journal of Scientific & Industrial Research, 56 (9), 523-539.