Last data updates: 18 December 2014

Ho, Y.S. (2005), Effect of pH on lead removal from water using tree fern as the sorbent. Bioresource Technology, 96 (11), 1292-1296.

| Document type: Article | Language: English | Cited references: 15 | Times cited: 88 | Times self cited: 3 |
| --- | --- | --- | --- | --- |

Abstract: The sorption of lead from water onto an agricultural by-product, tree fern, was examined as a function of pH. The sorption processes were carried out using an agitated and baffled system. Pseudo-second-order kinetic analyses were performed to determine the rate constant of sorption, the equilibrium sorption capacity, and the initial sorption rate. Application of the pseudo-second-order kinetics model produced very high coefficients of determination. Results showed the efficiency of tree fern as a sorbent for lead. The optimum pH for lead removal was between 4 and 7, with pH 4.9 resulting in better lead removal. Ion exchange occurred in the initial reaction period. In addition, a relation between the change in the solution hydrogen ion concentration and equilibrium capacity was developed and is presented. (c) 2004 Elsevier Ltd. All rights reserved.

Keywords: Biosorption, pH, Pseudo-Second-Order, Lead, Tree Fern, Adsorption, Metal-Ions, Activated Carbon, Heavy-Metals, Sorption, Copper, Equilibrium, Biosorption

Addresses: Ho YS, Taipei Med Univ, Sch Publ Hlth, 250 Wu Hsing St, Taipei 11014, Taiwan

E-mail Addresses: ysho@tmu.edu.tw

- Guo, X.Y., Du, B., Wei, Q., Yang, J., Hu, L.H., Yan, L.G. and Xu, W.Y. (2014), Synthesis of amino functionalized magnetic graphenes composite material and its application to remove Cr(VI), Pb(II), Hg(II), Cd(II) and Ni(II) from contaminated water. Journal of Hazardous Materials, 278), 211-220.

- Jafari, S.A. and Cheraghi, S. (2014), Mercury removal from aqueous solution by dried biomass of indigenous Vibrio parahaemolyticus PG02: Kinetic, equilibrium, and thermodynamic studies. International Biodeterioration & Biodegradation, 92), 12-19.

- Shin, W.S. and Kim, Y.K. (2014), Biosorption characteristics of heavy metals (Ni2+, Zn2+, Cd2+, Pb2+) from aqueous solution by Hizikia fusiformis. Environmental Earth Sciences, 71 (9), 4107-4114.

- Barbooti, M.M., Su, H., Punamiya, P. and Sarkar, D. (2014), Oxytetracycline sorption onto Iraqi montmorillonite. International Journal of Environmental Science and Technology, 11 (1), 69-76.

- Bo, T., Zhang, L.X., Zhu, X.Y., He, X.H., Tao, Y., Zhang, J.T. and Li, D.P. (2014), Lead ions removal from aqueous solution in a novel bioelectrochemical system with a stainless steel cathode. Rsc Advances, 4 (77), 41135-41140.

- Elkady, M.F., El-Sayed, E.M., Farag, H.A. and Zaatout, A.A. (2014), Assessment of Novel Synthetized Nanozirconium Tungstovanadate as Cation Exchanger for Lead Ion Decontamination. Journal of Nanomaterials, .

- Miranda, J., Krishnakumar, G. and Gonsalves, R. (2013), Lead sorption by living biomass of Chroococcus multicoloratus and Oscillatoria trichoides: kinetics and equilibrium studies. Annals of Microbiology, 63 (2), 591-605.

- Ghaedi, M., Hajati, S., Karimi, F., Barazesh, B. and Ghezelbash, G. (2013), Equilibrium, kinetic and isotherm of some metal ion biosorption. Journal of Industrial and Engineering Chemistry, 19 (3), 987-992.

- Huang, J.H., Wu, X.F., Zha, H.W., Yuan, B. and Deng, S.G. (2013), A hypercrosslinked poly(styrene-co-divinylbenzene) PS resin as a specific polymeric adsorbent for adsorption of 2-naphthol from aqueous solutions. Chemical Engineering Journal, 218), 267-275.

- Cankilic, M.Y., Karabacak, R.B., Tay, T. and Kivanc, M. (2013), Sorption of lead ions from aqueous solution onto Enterococcus faecium biomass. Water Science and Technology, 68 (7), 1550-1555.

- Ding, Y., Wang, D., Jing, D.B., Huang, Z.D. and Wang, Z. (2013), Adsorption of Aquatic Cadmium (II) by Chestnut Inner Shell. 2013 Third International Conference on Intelligent System Design and Engineering Applications (Isdea), ), 222-226.

- Siyal, A.N., Memon, S.Q., Amanullah, M., Pirzada, T., Parveen, S. and Sodho, N.A. (2013), Multi-variant sorption optimization for the uptake of Pb(II) ions by Jamun Seed Waste. Polish Journal of Chemical Technology, 15 (1), 15-21.

- Wang, Y., Wang, X.J., Wang, X., Liu, M.A., Yang, L.Z., Wu, Z., Xia, S.Q. and Zhao, J.F. (2012), Adsorption of Pb(II) in aqueous solutions by bamboo charcoal modified with KMnO4 via microwave irradiation. Colloids and Surfaces A-Physicochemical and Engineering Aspects, 414), 1-8.

- Miranda, J., Krishnakumar, G. and D'Silva, A. (2012), Removal of Pb2+ from aqueous system by live Oscillatoria laete-virens (Crouan and Crouan) Gomont isolated from industrial effluents. World Journal of Microbiology & Biotechnology, 28 (10), 3053-3065.

- Shahid, M., Pinelli, E. and Dumat, C. (2012), Review of Pb availability and toxicity to plants in relation with metal speciation; role of synthetic and natural organic ligands. Journal of Hazardous Materials, 219), 1-12.

- Ding, Y., Jing, D.B., Gong, H.L., Zhou, L.B. and Yang, X.S. (2012), Biosorption of aquatic cadmium(II) by unmodified rice straw. Bioresource Technology, 114), 20-25.

- Saka, C., Sahin, O. and Kucuk, M.M. (2012), Applications on agricultural and forest waste adsorbents for the removal of lead (II) from contaminated waters. International Journal of Environmental Science and Technology, 9 (2), 379-394.

- Mahmoud, M.E., Yakout, A.A., bdel-Aal, H. and Osman, M.M. (2012), High performance SiO2-nanoparticles-immobilized-Penicillium funiculosum for bioaccumulation and solid phase extraction of lead. Bioresource Technology, 106), 125-132.

- Al-Qahtani, K.M. (2012), Biosorption of Cd+2 and Pb+2 on Cyperus laevigatus: application of factorial design analysis. Life Science Journal-Acta Zhengzhou University Overseas Edition, 9 (4), 860-868.

- Ravichandran, P., Sowmya, A. and Meenakshi, S. (2012), Equilibrium and Kinetic Studies on the Removal of Basic Violet 10 from Aqueous Solutions Using Activated Carbons Prepared from Industrial Wastes. Bioremediation Journal, 16 (2), 86-96.

- Modenes, A.N., Espinoza-Quinones, F.R., Trigueros, D.E.G., Pietrobelli, J.M.T.A., Lavarda, F.L., Ravagnani, M.A.S.S. and Bergamasco, R. (2012), Binary Adsorption of a Zn(II)-Cu(II) Mixture onto Egeria densa and Eichhornia crassipes: Kinetic and Equilibrium Data Modeling by PSO. Separation Science and Technology, 47 (6), 875-885.

- Siyal, A.N., Memon, S.Q. and Khaskheli, M.I. (2012), Optimization and equilibrium studies of Pb(II) removal by Grewia Asiatica seed: a factorial design approach. Polish Journal of Chemical Technology, 14 (1), 71-77.

- Depci, T., Kul, A.R., Onal, Y., Disli, E., Alkan, S. and Turkmenoglu, Z.F. (2012), Adsorption of Crystal Violet from Aqueous Solution on Activated Carbon Derived from Golbasi Lignite. Physicochemical Problems of Mineral Processing, 48 (1), 253-270.

- Parvathi, C., Maruthavanan, T., Sivamani, S. and Prakash, C. (2011), Biosorption Studies for the Removal of Malachite Green from its Aqueous Solution by Activated Carbon Prepared from Cassava Peel. E-Journal of Chemistry, 8), S61-S66.

- Benaissa, H. and Elouchdi, M.A. (2011), Biosorption of copper (II) ions from synthetic aqueous solutions by drying bed activated sludge. Journal of Hazardous Materials, 194), 69-78.

- Mandavi, M., Ahmad, M.B., Haron, M.J., Ab Rahman, M.Z. and Shameli, K. (2011), Equilibrium Isotherm Studies for the Uptake of Pb(II) and Cd(II) Onto Lignocellulosic Biosorbent from Waste Water. Research Journal of Chemistry and Environment, 15 (2), 251-255.

- Mahdavi, M., Ahmad, M.B., Haron, M.J., Rahman, M.Z. and Shameli, K. (2011), Equilibrium Isotherm Studies for the Uptake of Pb(II) and Cd(II) Onto Lignocellulosic Biosorbent from Waste Water. Research Journal of Chemistry and Environment, 15 (2), 332-336.

- Singanan, M. (2011), Removal of lead(II) and cadmium(II) ions from wastewater using activated biocarbon. Scienceasia, 37 (2), 115-119.

- El-Said, A.G., Badawy, N.A., bdel-Aal, A.Y. and Garamon, S.E. (2011), Optimization parameters for adsorption and desorption of Zn(II) and Se(IV) using rice husk ash: kinetics and equilibrium. Ionics, 17 (3), 263-270.

- Modenes, A.N., Espinoza-Quinones, F.R., Trigueros, D.E.G., Lavarda, F.L., Colombo, A. and Mora, N.D. (2011), Kinetic and equilibrium adsorption of Cu(II) and Cd(II) ions on Eichhornia crassipes in single and binary systems. Chemical Engineering Journal, 168 (1), 44-51.

- Zhang, D.Y., Pan, X.L., Zhao, L. and Mu, G.J. (2011), Biosorption of Antimony (Sb) by the Cyanobacterium Synechocystis sp. Polish Journal of Environmental Studies, 20 (5), 1353-1358.

- Yazid, H., Sadaoui, Z. and Maachi, R. (2011), Removal of Cadmium (II) Ions from Aqueous Phase by Biosorption on Biological Activated Dates' Pedicels (Kinetic, Equilibrium and Thermodynamic Study). International Journal of Chemical Reactor Engineering, 9 .

- Hubbe, M.A., Hasan, S.H. and Ducoste, J.J. (2011), Cellulosic Substrates for Removal of Pollutants from Aqueous Systems: A Review. 1. Metals. Bioresources, 6 (2), 2161-U2914.

- Saka, C., Sahin, O., Demir, H. and Kahyaoglu, M. (2011), Removal of Lead(II) from Aqueous Solutions using Pre-boiled and Formaldehyde-Treated Onion Skins as a New Adsorbent. Separation Science and Technology, 46 (3), 507-517.

- Haron, M.J., Tiansin, M., Ibrahim, N.A., Kassim, A., Yunus, W.M.Z.W. and Talebi, S.M. (2011), Sorption of Pb(II) by poly(hydroxamic acid) grafted oil palm empty fruit bunch. Water Science and Technology, 63 (8), 1788-1793.

- Ozsoy, H.D. (2010), Biosorptive removal of Hg(II) ions by Rhizopus oligosporus produced from corn-processing wastewater. African Journal of Biotechnology, 9 (51), 8783-8790.

- Malarvizhi, R. and Ho, Y.S. (2010), The influence of pH and the structure of the dye molecules on adsorption isotherm modeling using activated carbon. Desalination, 264 (1-2), 97-101.

- Mohy-Eldin, M.S., Elkady, M.F., bu-Saied, M.A., Rahman, A.M.A., Soliman, E.A., Elzatahry, A.A. and Youssef, M.E. (2010), Removal of Cadmium Ions from Synthetic Aqueous Solutions with a Novel Nanosulfonated Poly(glycidyl methacrylate) Cation Exchanger: Kinetic and Equilibrium Studies. Journal of Applied Polymer Science, 118 (6), 3111-3122.

- Zakeri, F., Noghabi, K.A., Sadeghizadeh, M., Kardan, M.R., Masoomi, F., Farshidpour, M.R. and Atarilar, A. (2010), Serratia sp. ZF03: An efficient radium biosorbent isolated from hot-spring waters in high background radiation areas. Bioresource Technology, 101 (23), 9163-9170.

- Ofomaja, A.E. and Naidoo, E.B. (2010), Biosorption of lead(II) onto pine cone powder: Studies on biosorption performance and process design to minimize biosorbent mass. Carbohydrate Polymers, 82 (4), 1031-1042.

- Ofomaja, A.E. (2010), Biosorption studies of Cu(II) onto Mansonia sawdust: Process design to minimize biosorbent dose and contact time. Reactive & Functional Polymers, 70 (11), 879-889.

- Bryaskova, R., Georgieva, N. and Peshev, D. (2010), Removal of cadmium and copper ions by Trichosporon cutaneum R57 cells immobilized onto polyvinyl alcohol/tetraethoxysilane hybrid matrices. Central European Journal of Chemistry, 8 (5), 1053-1058.

- Bai, Y.H., Sun, Q.H., Xing, R., Wen, D.H. and Tang, X.Y. (2010), Removal of pyridine and quinoline by bio-zeolite composed of mixed degrading bacteria and modified zeolite. Journal of Hazardous Materials, 181 (1-3), 916-922.

- Ghaedi, M., Ghezelbash, G.R., Marahel, F., Ehsanipour, S., Najibi, A. and Soylak, M. (2010), Equilibrium, Thermodynamic, and Kinetic Studies on Lead (II) Biosorption from Aqueous Solution by Saccharomyces cerevisiae Biomass. Clean-Soil Air Water, 38 (9), 877-885.

- Ofomaja, A.E. (2010), Intraparticle diffusion process for lead(II) biosorption onto mansonia wood sawdust. Bioresource Technology, 101 (15), 5868-5876.

- Saeed, A., Sharif, M. and Iqbal, M. (2010), Application potential of grapefruit peel as dye sorbent: Kinetics, equilibrium and mechanism of crystal violet adsorption. Journal of Hazardous Materials, 179 (1-3), 564-572.

- Huang, L.Z., Zeng, G.M., Huang, D.L., Li, L.F., Du, C.Y. and Zhang, L. (2010), Biosorption of cadmium(II) from aqueous solution onto Hydrilla verticillata. Environmental Earth Sciences,  60 (8), 1683-1691.

- Rao, K.S., Anand, S. and Venkateswarlu, P. (2010), Adsorption of Cadmium(Ii) Ions from Aqueous Solution by Tectona Grandis Lf (Teak Leaves Powder). Bioresources, 5 (1), 438-U26.

- Qaiser, S., Saleemi, A.R. and Umar, M. (2009), Biosorption of lead(II) and chromium(VI) on groundnut hull: Equilibrium, kinetics and thermodynamics study. Electronic Journal of Biotechnology, 12 (4.

- Pietrobelli, J.M.T.D., Modenes, A.N., Fagundes-Klen, M.R. and Espinoza-Quinones, F.R. (2009), Cadmium, Copper and Zinc Biosorption Study by Non-Living Egeria densa Biomass. Water Air and Soil Pollution , 202 (1-4), 385-392.

- Alyuz, B. and Veli, S. (2009), Kinetics and equilibrium studies for the removal of nickel and zinc from aqueous solutions by ion exchange resins. Journal of Hazardous Materials, 167 (1-3), 482-488.

- Ozcan, A.S., Tunali, S., Akar, T. and Ozcan, A. (2009), Biosorption of lead(II) ions onto waste biomass of Phaseolus vulgaris L.: estimation of the equilibrium, kinetic and thermodynamic parameters. Desalination, 244 (1-3), 188-198.

- Qaiser, S., Saleemi, A.R. and Umar, M. (2009), Biosorption of lead from aqueous solution by Ficus religiosa leaves: Batch and column study. Journal of Hazardous Materials, 166 (2-3), 998-1005.

- Zhang, J., Xie, S.D. and Ho, Y.S. (2009), Removal of fluoride ions from aqueous solution using modified attapulgite as adsorbent. Journal of Hazardous Materials, 165 (1-3), 218-222.

- Wang, M.Y., Wang, Z. and Guo, Z.C. (2009), Regularity and Mechanism of Pb Electrodeposition Intensified by Super Gravity Field. Acta Physico-Chimica Sinica, 25 (5), 883-889.

- Hashimoto, Y., Taki, T. and Sato, T. (2009), Sorption of dissolved lead from shooting range soils using hydroxyapatite amendments synthesized from industrial byproducts as affected by varying pH conditions. Journal of Environmental Management, 90 (5), 1782-1789.

- Sreejalekshmi, K.G., Krishnan, K.A. and Anirudhan, T.S. (2009), Adsorption of Pb(II) and Pb(II)-citric acid on sawdust activated carbon: Kinetic and equilibrium isotherm studies. Journal of Hazardous Materials, 161 (2-3), 1506-1513.

- Ramakrishnan, M. and Nagarajan, S. (2009), Utilisation of Flame Tree Waste Biomass for the Removal of Hg(II) from Water. Acta Chimica Slovenica, 56 (1), 282-287.

- Kaczala, F., Marques, M. and Hogland, W. (2009), Lead and vanadium removal from a real industrial wastewater by gravitational settling/sedimentation and sorption onto Pinus sylvestris sawdust. Bioresource Technology, 100 (1), 235-243.

- Joseph, O., Rouez, M., Metivier-Pignon, H., Bayard, R., Emmanuel, E. and Gourdon, R. (2009), Adsorption of heavy metals on to sugar cane bagasse: Improvement of adsorption capacities due to anaerobic degradation of the biosorbent. Environmental Technology, 30 (13), 1371-1379.

- Pura, S. and Atun, G. (2009), Adsorptive Removal of Acid Blue 113 and Tartrazine by Fly Ash from Single and Binary Dye Solutions. Separation Science and Technology, 44 (1), 75-101.

- Modenes, A.N., Pietrobelli, J.M.T.D. and Espinoza-Quinones, F.R. (2009), Cadmium biosorption by non-living aquatic macrophytes Egeria densa. Water Science and Technology, 60  (2), 293-300.

- Aroua, M.K., Leong, S.P.P., Teo, L.Y., Yin, C.Y. and Daud, W.M.A.W. (2008), Real-time determination of kinetics of adsorption of lead(II) onto palm shell-based activated carbon using ion selective electrode. Bioresource Technology, 99 (13), 5786-5792.

- Ozsoy, H.D., Kumbur, H., Saha, B. and van Leeuwen, J.H. (2008), Use of Rhizopus oligosporus produced from food processing wastewater as a biosorbent for Cu(II) ions removal from the aqueous solutions. Bioresource Technology, 99 (11), 4943-4948.

- Pehlivan, E., Yanik, B.H., Ahmetli, G. and Pehlivan, M. (2008), Equilibrium isotherm studies for the uptake of cadmium and lead ions onto sugar beet pulp. Bioresource Technology, 99 (9), 3520-3527.

- Serencam, H., Gundogdu, A., Uygur, Y., Kemer, B., Bulut, V.N., Duran, C., Soylak, M. and Tufekci, M. (2008), Removal of cadmium from aqueous solution by Nordmann fir (Abies nordmanniana (Stev.) Spach. Subsp nordmanniana) leaves. Bioresource Technology, 99 (6), 1992-2000.

- Inbaraj, B.S., Chiu, C., Ho, G.H., Yang, J. and Chen, B.H. (2008), Effects of temperature and pH on adsorption of basic brown 1 by the bacterial biopolymer poly(gamma-glutamic acid). Bioresource Technology, 99 (5), 1026-1035.

- Solener, M., Tunali, S., Ozcan, A.S., Ozcan, A. and Gedikbey, T. (2008), Adsorption characteristics of lead(II) ions onto the clay/poly(methoxyethyl)acrylamide (PMEA) composite from aqueous solutions. Desalination, 223 (1-3), 308-322.

- Kilic, M., Keskin, M.E., Mazlum, S. and Mazlum, N. (2008), Effect of conditioning for Pb(II) and Hg(II) biosorption on waste activated sludge. Chemical Engineering and Processing, 47 (1), 31-40.

- Ornek, A., Ozacar, M. and Sengil, I.A. (2007), Adsorption of lead onto formaldehyde or sulphuric acid treated acorn waste: Equilibrium and kinetic studies. Biochemical Engineering Journal, 37 (2), 192-200.

- Ahluwalia, S.S. and Goyal, D. (2007), Microbial and plant derived biomass for removal of heavy metals from wastewater. Bioresource Technology, 98 (12), 2243-2257.

- Wang, L. and Wang, A.Q. (2007), Adsorption characteristics of Congo Red onto the chitelsan/montmorillonite nanocomposite. Journal of Hazardous Materials, 147 (3), 979-985.

- Vieira, D.M., da Costa, A.C.C., Henriques, C.A., Cardoso, V.L. and de Franca, F.P. (2007), Biosorption of lead by the brown seaweed Sargassum filipendula - batch and continuous pilot studies. Electronic Journal of Biotechnology, 10 (3), 368-375.

- Anirudhan, T.S., Unnithan, M.R., Divya, L. and Senan, P. (2007), Synthesis and characterization of polyacrylamide-grafted coconut coir pith having carboxylate functional group and adsorption ability for heavy metal ions. Journal of Applied Polymer Science, 104 (6), 3670-3681.

- Gode, F. (2007), Heavy metal removal from aqueous solutions by adsorption using montmorillonite. Asian Journal of Chemistry, 19 (3), 2211-2224.

- Ofomaja, A.E. and Ho, Y.S. (2007), Effect of pH on cadmium biosorption by coconut copra meal. Journal of Hazardous Materials, 139 (2), 356-362.

- Karadag, D. (2007), Modeling the mechanism, equilibrium and kinetics for the adsorption of Acid Orange 8 onto surfactant-modified clinoptilolite: The application of nonlinear regression analysis. Dyes and Pigments, 74 (3), 659-664.

- Ozcan, A.S., Ozcan, A., Tunali, S., Akar, T., Kiran, I. and Gedikbey, T. (2007), Adsorption potential of lead(II) ions from aqueous solutions onto Capsicum annuum seeds. Separation Science and Technology, 42 (1), 137-151.

- Inbaraj, B.S., Chien, J.T., Ho, G.H., Yang, J. and Chen, B.H. (2006), Equilibrium and kinetic studies on sorption of basic dyes by a natural biopolymer poly(gamma-glutamic acid). Biochemical Engineering Journal, 31 (3), 204-215.

- Azizian, S. (2006), A novel and simple method for finding the heterogeneity of adsorbents on the basis of adsorption kinetic data. Journal of Colloid and Interface Science, 302 (1), 76-81.

- Inbaraj, B.S., Chiu, C.P., Ho, G.H., Yang, J. and Chen, B.H. (2006), Removal of cationic dyes from aqueous solution using an anionic poly-gamma-glutamic acid-based adsorbent. Journal of Hazardous Materials, 137 (1), 226-234.

- Ozsoy, H.D. and Kumbur, H. (2006), Adsorption of Cu(II) ions on cotton boll. Journal of Hazardous Materials, 136 (3), 911-916.

- Southichak, B., Nakano, K., Nomura, M., Chiba, N. and Nishimura, O. (2006), Phragmites australis: A novel biosorbent for the removal of heavy metals from aqueous solution. Water Research, 40 (12), 2295-2302.

- Benaissa, H. (2006), Screening of new sorbent materials for cadmium removal from aqueous solutions. Journal of Hazardous Materials, 132 (2-3), 189-195.

- Abu Al-Rub, F.A. (2006), Biosorption of zinc on palm tree leaves: Equilibrium, kinetics, and thermodynamics studies. Separation Science and Technology, 41 (15), 3499-3515.

- Machida, M., Yamazaki, R., Aikawa, M. and Tatsumoto, H. (2005), Role of minerals in carbonaceous adsorbents for removal of Pb(II) ions from aqueous solution. Separation and Purification Technology, 46 (1-2), 88-94.

- Ozcan, A., Ozcan, A.S., Tunali, S., Akar, T. and Kiran, I. (2005), Determination of the equilibrium, kinetic and thermodynamic parameters of adsorption of copper(II) ions onto seeds of Capsicum annuum. Journal of Hazardous Materials, 124 (1-3), 200-208.